## Slide 1
Fluid Mechanics CEE 3311
LECTURE 17
Flow in Pipes
(Internal Flows)
L. Handia

## Slide 2: Boundary layer: Laminar flow

## Slide 3: Boundary layer: Turbulent flow
The viscous sublayer is a layer where shear is predominantly due to viscosity alone. It is extremely thin, usually only a few hundredths of a mm, but its effect is great because of the very steep velocity gradient within it and because τ = μ du/dy in that region

## Slide 4
If the head loss in a given length of uniform pipe is measured at different velocities, it will be found that, as long as the velocity is low enough to secure laminar ﬂow, the head loss, due to friction, will be directly proportional to the velocity, as shown in the Fig.
But with increasing velocity, at some point B, where visual observation of dye injected in a transparent tube would show that the ﬂow changes from laminar to turbulent, there will be an abrupt increase in the rate at which the head loss varies.
Laminar and turbulent flow

## Slide 5
Laminar and turbulent flow
It is thus seen that for laminar ﬂow the drop in energy due to friction varies as V, while for turbulent ﬂow the friction varies as Vn, where n ranges from about 1.75 to 2. The lower value of 1.75 for turbulent ﬂow is found for pipes with very smooth walls; as the wall roughness increases, the value of n increases up to its maximum value of 2.
Point B is known as the higher critical point, and A as the lower critical point.
If these two variables are plotted on log-log paper, it will be found that, after a certain transition region (BCA) has been passed, lines will be obtained with slopes ranging from about 1.75 to 2.00.

## Slide 6
However, velocity is not the only factor that determines whether the ﬂow is laminar or turbulent. The criterion is Reynolds number, which has been discussed in previous lectures.
For a circular pipe the signiﬁcant linear dimension L is usually taken as the diameter D, and thus
Laminar and turbulent flow

## Slide 7
Critical Reynolds Number
The upper critical Reynolds number, corresponding to point B of Fig. 17.x is really indeterminate and depends upon the care taken to prevent any initial disturbance from affecting the ﬂow. Its value is normally about 4000 but laminar ﬂow in circular pipes has been maintained up to values of Re as high as 50,000. However, in such cases this type of ﬂow is inherently unstable. 'the least disturbance will transform it instantly into turbulent ﬂow.
Laminar and turbulent flow
On the other hand, it is practically impossible for turbulent ﬂow in a straight pipe to persist at values of Re much below 2000, because any turbulence that is set will be damped out by viscous friction.
However, for normal cases of ﬂow in straight pipes of uniform diameter and usual roughness, the critical value may be taken as Recrit = 2000.

## Slide 10: Laminar and turbulent flow

## Slide 11: Hydraulic radius
For conduits having noncircular cross sections, some value other than the diameter must be used for the linear dimension in the Reynolds number. Such a characteristic is the hydraulic radius, deﬁned as
where A is the cross-sectional area of the ﬂowing ﬂuid, and P is the wetted perimeter, that portion of the perimeter of the cross section where there is contact between ﬂuid and solid boundary.

## Slide 12
Laminar flow (Hagen-Poiseuille’s formula)
Consider steady flow in a conduit of uniform cross section A, not necessarily circular. The pressures at sections 1 and 2 are P1 and P2, respectively. The distance between them is L. for equilibrium in steady flow, the summation of forces acting on any fluid element must be equal to zero (i.e., ΣF = ma = 0). Thus in the direction of flow

## Slide 13
Where and . Therefore equation 11.1 reduces to
Laminar flow (Hagen-Poiseuille’s formula)
sin

## Slide 14
11.3
where
Laminar flow (Hagen-Poiseuille’s formula)

## Slide 15
Laminar flow (Hagen-Poiseuille’s formula)
Since the gradient itself, dP*/ds, is negative (piezometric pressure decreases in the direction of flow) and constant across the section for uniform flow, it follows that - dP*/ds will be positive and constant across the pipe. At the wall of the pipe, r = R, the shear stress is
11.3
11.4

## Slide 16
Laminar flow (Hagen-Poiseuille’s formula)
Thus, dividing 11.3 by 11,4 gives
11.5
Consequently varies linearly with r from a value of zero at the centerline of the pipe to a maximum at the wall. This distribution of stress is represented graphically in Fig 11.2
Note: in the derivation of 11.5 no restrictions concerning laminar or turbulent flow have been made. Therefore, the law of linear distribution of shear stress over a circular section, represented by 11,5, holds for both flow conditions

## Slide 17
Steady laminar flow in circular pipes
From Newton’s law of viscosity . Substituting this into 11.3 gives
11.6
Noting that (since velocity decreases in the direction of r Fig 11.3), 11.6 becomes
11.7
Separating variables and assuming a Newtonian fluid (
11.8

## Slide 18
Steady laminar flow in circular pipes
11.8
Boundary condition: at (no slip)
11.9
11.9 indicates that the velocity distribution for laminar flow in a pipe is parabolic across the section with the maximum velocity at the centre of the pipe Fig 11.3

## Slide 19
Steady laminar flow in circular pipes
Of far more interest than the velocity at a particular point is the total discharge through it. The discharge dQ through the annular space between radii r and r + dr is
The discharge through the entire cross section is therefore
Thus 11.11 Hagen-Poiseuille Formula
For a length L of the pipe over which the piezometric pressure drops from P1 to P2, the equation may be written as
or more suitable
11.12 where D is the diameter
dr

## Slide 20
Laminar flow (Hagen-Poiseuille’s formula)

## Slide 21
Steady laminar flow in circular pipes
Eq. 11.12 is strictly applicable only to the laminar flow of constant density fluids and laminar flow which is "fully developed". From the entrance of the pipe the fluid has to traverse a certain distance before the parabolic velocity distribution is established.
The formula of Eq.11.12 is applied for many types of viscometer, a device for determining the viscosity of a fluid.
Rearranging the Hagen-Poiseuille law as
shows that for a laminar flow in a circular tube, the viscosity can easily be determined after the difference of piezometric pressure between the ends of a capillary tube has been measured by a manometer. When the fluid is a liquid, the volume flow rate Q may be determined simply by collecting and measuring the quantity passing through the tube in a certain time.

## Slide 22
Steady laminar flow in circular pipes
From 11.11 the mean velocity may be calculated
11.13
From 11.9 it can be seen that the maximum velocity vmax occurs in the centre of the pipe, where r = 0. Thus
11.14
Hence, from 11.13 and 11.14 it may be concluded that v = vmax / 2.
For a length L of the pipe, it follows from 11.13 that
11.15
In terms of “heads” (with )
11.16
Where head loss due to frictional resistance of the pipe.

## Slide 27
Turbulent flow (Darcy-Weisbach formula
Velocity profile in turbulent flow
In Fig. 8.10 may be seen profiles for both a smooth and a rough pipe.
Comparing the turbulent-flow velocity profiles with the laminar-flow
velocity proﬁle (Fig. 8.10) shows the turbulent-ﬂow proﬁles to be much ﬂatter near the central portion of the pipe and steeper near the wall.
It is also noticeable that the turbulent proﬁle for the smooth pipe is ﬂatter near the central section (i.e., blunter) than for the rough pipe.
In contrast, the velocity proﬁle in laminar ﬂow is independent of pipe roughness.

## Slide 28
Turbulent flow (Darcy-Weisbach formula
In the previous lecture 16, the shear force on a flat plate, friction drag, was expressed as
The shear stress on a flat plate is then .
For pipe flow it is customary to express τ0 in a similar manner; however, we use the mean velocity as the reference velocity, and the coefficient of proportionality is given as f/4 instead of Cf. Here f is called the resistance coefficient, or more usual, the friction factor of the pipe.

## Slide 29
Turbulent flow (Darcy-Weisbach formula
Thus we have
12.5
In section on Laminar Flow it was found that the shear stress at the wall of the pipe
11.4
Equating 12.5 and 11.4

## Slide 30
Turbulent flow (Darcy-Weisbach formula
12.6 Darcy Weisbach Equation
where hL = head loss created by viscous effects and is equal to the change of piezometric head.
Although the Darcy Weisbach Equation is for turbulent flow, it can still be used for laminar flow. For laminar flow, where (Eq.11.16), it can easily be shown that
f = 64/Re 12.7
Hence, if Re is less than 2,000 (laminar flow), one may use Eq. 12.6 with the value of f as given by Eq. 12.7

## Slide 31
The friction factor f depends on the various quantities that affect the ﬂow, written as
f = f(ρ, μ, V, D, e) (7.6.24)
where the average wall roughness height e accounts for the influence of the wall roughness elements. A dimensional analysis, not covered in this course, provides us with
where e/D is the relative roughness.
Experimental data that relate the friction factor to the Reynolds number have been obtained for fully developed pipe ﬂow over a wide range of wall roughnesses. The results of these data are presented in Fig. 7.13, which is commonly referred to as the Moody diagram.
Chart (and equations) for friction factor

## Slide 34
There are several features of the Moody diagram that should be noted.
    For a given wall roughness, measured by the relative roughness e/D, there is a sufficiently large value of Re above which the friction factor is constant, thereby defining the completely turbulent regime. The average roughness element size e is substantially greater than the viscous wall layer thickness δv, so that viscous effects are not significant; the resistance to the flow is produced primarily by the drag of the roughness elements that protrude into the flow.
    For the smaller relative roughness e/D values it is observed that, as Re decreases, the friction factor increases in the transition zone and eventually becomes the same as that of a smooth pipe. The roughness elements become submerged in the viscous wall layer so that they produce little effect on the main flow.
    For Reynolds numbers less than 2000, the friction factor of laminar flow is shown. The critical zone couples the turbulent flow to the laminar flow and may represent an oscillating flow that alternately exists between turbulent and laminar flow.
    The e values in this diagram are for new pipes. With age a pipe will corrode and become fouled, changing both the roughness and the pipe diameter, with a resulting increase in the friction factor. Such factors should be included in design considerations; they will not be reviewed here.

## Slide 35
The following empirical equations represent the Moody diagram for Re > 4000:
Good approximations can be made for the head loss in conduits with noncircular cross sections by using the hydraulic radius R.
The transition zone equation (7.6.28) that couples the smooth pipe equation to the completely turbulent regime equation is known as the Colebrook equation. Note that Eq.7.6.26 is the Colebrook equation with e = 0, and Eq. 7.6.27 is the Colebrook equation
with Re = ∞.

## Slide 36
Three categories of problems can be identified for developed turbulent flow in a pipe length L:
A category 1 problem is straightforward and requires no iteration procedure when using the Moody diagram.
Category 2 and 3 problems are more like problems encountered in
engineering design situations and require an iterative trial-and-error process when using the Moody diagram.
An alternative to using the Moody diagram that avoids any trial-and-error process is made possible by empirically derived formulas. Perhaps the best of such formulas were presented by Swamee and Jain (1976) for pipe ﬂow; an explicit expression that provides
an approximate value for the unknown in each category above is as follows:
Solution of pipe flow problems by trials

## Slide 37
An alternative to using the Moody diagram that avoids any trial-and-error process is made possible by empirically derived formulas.
Perhaps the best of such formulas were presented by Swamee and Jain (1976) for pipe ﬂow; an explicit expression that provides an approximate value for the unknown in each category above is as follows:
Solution of pipe flow problems using empirical equations

## Slide 38
Equation 7.6.32 is as accurate as the Moody diagram, and Eqs. 7.6.31 and 7.6.33 are accurate to within approximately 2% of the Moody diagram. These tolerances are acceptable for engineering calculations. It is important to realize that the Moody diagram is based on experimental data that likely is accurate to within no more than 5%.
Hence the foregoing three formulas of Swamee and Jain, which can easily be input on a programmable hand-held calculator, are often used by design engineers.
Solution of pipe flow problems using empirical equations

## Slide 41
Minor losses in pipe flow

## Slide 42
Minor losses in pipe flow

## Slide 43
Minor losses in pipe flow