## Slide 1
Geologic structures

## Slide 2: Introduction
This lecture is devoted to review structures in rocks:
    Layering – bedding, foliation
    Folds
    Joints / fractures
    Faults

## Slide 3: Introduction…..contd.
These structures may be:
  Global, macro or micro
  Primary or secondary
  Primary Structures – those formed at same time as rock.
  Secondary Structures – those formed after formtion of rock.

## Slide 4: Primary Structures
Bedding – sedimentary rocks

## Slide 5: Primary Structures…..contd.

## Slide 6: Primary Structures…..contd.
Ripple Marks – sedimentary rocks.
Formed from currents and waves
Evidence usually preserved and found in rocks

## Slide 7: Primary Structures…..contd.
Layering – igneous rocks
As indicated earlier, primary structures form at the same time as the rock.

## Slide 8
Formed:
after formtion of rock
by tectonic stresses – confining stress / pressure – on rock / sediment when these are buried.
Tectonic processes create three types of directed stress.
Secondary Structures…..contd.

## Slide 9
Tectonic processes create three types of directed stress:
Compressive stress – common in convergent plate boundaries, where two plates converge and rock crumples.
Secondary Structures…..contd.

## Slide 10
Extensional stress (also called tensional stress) – pulls rock apart and is the opposite of tectonic compression.
  Rocks @ divergent plate boundary stretch and pull apart because they are subject to extensional stress.
Secondary Structures…..contd.

## Slide 11
Shear stress – acts in parallel but opposite directions.
  Shearing deforms rock by causing one part of a rock mass to slide past the other part – such as at transform boundary.
Secondary Structures…..contd.

## Slide 12
Secondary Structures…..contd.

## Slide 13
Folds
Faults
Joints
All of them occur in most rocks
These produce such structures as:
Secondary Structures…..contd.

## Slide 14: FOLDS

## Slide 15
Are bends / wave-like features in layered rocks.
usually result from compressive stresses,
usually occur as repeating patterns as in illustration using clay.
Folding always shortens horizontal distances in rock.
Folds

## Slide 16
Their Geometry includes (i) Limb, (ii) Hinge Line, and (iii) Axial Plane.
Folds…..contd.

## Slide 17
Fold Limbs – Anticline & Syncline
Folds…..contd.

## Slide 18
Open fold
Isoclinal fold
Overturned fold
Recumbent fold
Asymmetrical Folds
Symmetrical Folds
Interpreting Folds…..contd.

## Slide 19
  Open folds have limbs that have a gentle slope.
    The more open the folds, the less intense the stress involved
Interpreting Folds…..contd.

## Slide 20
  Isoclinal folds have limbs that are parallel to one another – implying intense compressive or shear stress
Interpreting Folds…..contd.

## Slide 21
  Overturned folds – when axial plane is inclined to such a degree that fold limbs dip in same direction – implying unequal compressive stresses…
Interpreting Folds…..contd.

## Slide 22
  Recumbent folds – those overturned to such an extent that limbs are essentially horizontal – indicating more intense compressive and/or shear stresses in one direction….
Interpreting Folds…..contd.

## Slide 23
A. Open (symmetrical)
Both limbs dip equally away from axial plane
B. Isoclinal
Both limbs are parallel to each other, regardless of dip of axial plane
C. Asymmetrical
One limb of fold dips more steeply than the other.
D. Overturned
Strata in one limb have tilted beyond vertical. Both limbs dip in same direction but at different angles.
E. Recumbent
Axial planes are horizontal or nearly so. Strata on lower limb of anticline and upper limb of syncline are upside down.
Axial plane
Axial plane
Axial plane
Axial plane
Overturned limb (steep dip)
Axial plane
Beds normal
Beds inverted
Normal limb (gentle dip)
Interpreting Folds…..contd.

## Slide 24: FAULTS

## Slide 25
Structures with major displacement of rock material along cracks in a rock. Or
Cracks in Earth's crust along which noticeable movement has occurred.
Faults

## Slide 26
  Geologists describe fault-movement in terms of direction of slippage.
    In a dip-slip fault, movement is parallel to the dip of the fault surface.
    A strike-slip fault indicates horizontal motion parallel to the strike of the fault surface.
    An oblique-slip fault has both strike-slip and dip-slip components.
Faults…..contd.

## Slide 27
Reverse Fault
A fault generally steeply inclined, along which hanging-wall block has moved relatively upward
Normal Fault
Movement is vertical
A fault generally steeply inclined, along which hanging-wall block has moved relatively downward
Reference block before faulting
Faults…..contd.

## Slide 28
Normal Fault
  Forces pull apart
  Middle block slides down
Reverse Fault
  Forces compress
  Middle block slides up
Dip-Slip Faults

## Slide 29
Normal & reverse faults – most common type
Usually distinguished from each other on basis of relative movement of the footwall block & hanging wall block.
    Footwall – surface underlying inclined fault plane.
    Hanging wall – surface overlying inclined fault plane.
Dip-Slip Faults…..contd.

## Slide 30
  In a normal fault:
  hanging-wall block moves downward relative to footwall block.
Normal Faults…..contd.

## Slide 31
  Results from tension / extension / lengthening of crust
Normal Faults…..contd.

## Slide 32
Normal Faults…..contd.

## Slide 33
  hanging-wall block moves upward relative to footwall block.
  Results from horizontal compressive forces
Reverse Faults

## Slide 34
Reverse Faults…..contd.

## Slide 35
  is a reverse fault with a low dip angle (< 30o) or even horizontal.
    typically moves or thrusts older rocks on top of younger rocks.
    results in an extreme shortening of crust.
Thrust Faults

## Slide 36
Thrust Model
Thrust Faults…..contd.

## Slide 37
  Results from shearing forces.
  movement (or slip) is predominantly horizontal & parallel to strike of the fault.
Strike-Slip Faults

## Slide 38
    displacement along a strike-slip fault is either left-lateral or right-lateral and can be determined by looking across fault.
      Left-lateral fault – when movement on other side of fault line is to the left.
      Right-lateral fault – when movement on other side of fault line is to the right.
Strike-Slip Faults…..contd.

## Slide 39
Right-lateral fault
Left-lateral fault
Strike-Slip Faults…..contd.

## Slide 40: JOINTS

## Slide 41
Crack surfaces or breaks in rock along which no movement has taken place
Result from tectonic forces, e.g. Compressive, tensional or shearing
Joints…..contd.

## Slide 42
are one of the most commonly observed structures in rocks.
Where joints are oriented approximately parallel to one another, they are called a joint set
Joints…..contd.

## Slide 43
Rock displaying Folding, jointing, faulting
Joints…..contd.

## Slide 44: Measurement of Geologic Structures

## Slide 45: Strike and Dip
According to the principle of original horizontality, sedimentary rocks are deposited as horizontal beds or strata.
  Where these originally horizontal rocks are found tilted, this must have occurred after deposition and lithification.

## Slide 46: Strike and Dip…..(2)
Strike: the compass direction of a line formed by the intersection of an inclined plane with a horizontal plane.

## Slide 47: Strike and Dip…..(3)
    Strike: measured in reference to northerly direction by degrees from 0o – 90o east or west.

## Slide 48: Strike and Dip…..(4)
Angle of Dip: a measurement downward from the horizontal plane to the bedding plane.
  Dip Direction: compass direction in which the angle of dip is measured.

## Slide 49: Strike and Dip…..(10)

## Slide 50: Strike and Dip…..(9)

## Slide 51: Strike and Dip…..(6)
Structural Dome / Structural Basin?

## Slide 52: Strike and Dip…..(7)
Structural Dome &....
...Structural Basin

## Slide 53: Strike and Dip…..(8)
Sedimentary layering dips away from a dome in all directions, and the outcrop pattern is circular or elliptical.
Layers dip toward the centre of a basin.

## Slide 54: Significance of GEOLOGIC STRUCTURES in engineering practice

## Slide 55
Challenges posed by Geologic Structures...
They act as conduits & stores for groundwater

## Slide 56
They act as conduits & stores for groundwater
Challenges posed by Geologic Structures...

## Slide 57
If sedimentary rock layers dip in the same direction as slope, upper layers may slide over the lower ones.
(A) If road cut undermines slope, where rocks dip parallel to slope, dipping rock provides good sliding surface.
A
B
Challenges posed by Geologic Structures...
(B) Slope will remain stable even when undermined if rock layers dip away from cut.

## Slide 58
They may impair performance of engineering structures, if not adequately taken into consideration
Challenges posed by Geologic Structures...

## Slide 59
They may act as conduits for contaminants to the groundwater store (aquifer)
Challenges posed by Geologic Structures...

## Slide 60
G.S. can also be a problem to mining. For instance;
occurrence of joints, bedding and/or faults might cause failure of slopes.
they might allow water to flow from surface into mine openings. This inflow might not only add costs to operations, but may also flood mines….
Challenges posed by Geologic Structures...

## Slide 61
Geologic structures:
come in different forms – folds, faults joints
can pause problems in drilling for water such as hole collapse;
act as passages for solutions from which mineral deposits are formed by precipitation.
Some Concluding Remarks

## Slide 62: End of Lecture