## Slide 1: EEE3131 Digital Electronics
Lecture 5 : VHDL
Instructor: George ZIBA
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Email: george.ziba@unza.zm
0976854627

## Slide 2
Objectives
At the end of this lecture the student should be able:
To understand why we need HDLs,
To understand the application of HDLs

## Slide 3
Introduction
Today design of digital systems is done by HDLs such as VHDL or Verilog unlike the traditional way of manually connecting discrete components on printed circuit boards.
VHDL is a hardware description language (HDL) and not a programming language, though its format is similar to popular programming languages.
To be able to manage complex designs quickly and without errors, the use of VHDL software packages becomes inevitable.

## Slide 4
CAD for Hardware Description
There are many CAD packages for describing hardware but the most popular and widely used are:
VHDL translated as Very high speed integrated circuits Hardware Description Language.
Verilog

## Slide 5
HDLs
A hardware description language is inherently parallel (not procedural)i.e. its commands, which correspond to logic gates are executed in parallel as soon as a new input arrives.
It also allows the incorporation of timing specifications (gate delays).
It also describes the system as an interconnection of different components but all done inside a chip.

## Slide 6
Why do we need HDLs?
To automate much of the traditional design and debugging of a digital system methodology.
For specifying, modeling, designing, synthesizing, documenting and simulating digital systems.

## Slide 7: Basic Language Elements
Comments are preceded by two consecutive hyphens ( -- ) and are terminated at the end of the line.
Example:
-- This is a comment

## Slide 8: Identifiers
VHDL identifier syntax:
A sequence of one or more uppercase letters, lowercase letters, digits, and the underscore
Upper and lowercase letters are treated the same (i.e., case insensitive)
The first character must be a letter
The last character cannot be the underscore
Two underscores cannot be together

## Slide 9: Data Objects
There are three kinds of data objects: signals, variables, and constants.
The data object SIGNAL represents logic signals on a wire in the circuit. A signal does not have memory; thus, if the source of the signal is removed, the signal will not have a value.
A VARIABLE object remembers its content and is used for computations in a behavioral model.
A CONSTANT object must be initialized with a value when declared and this value cannot be changed.

## Slide 10: BIT and BIT_VECTOR
The BIT and BIT_VECTOR types are predefined in VHDL. Objects of these types can have the values ‘0’ or ‘1’.The BIT_VECTOR type is simply a vector of type BIT. A vector with all bits having the same value can be obtained using the OTHERS keyword.
Example:
  SIGNAL x: BIT;
  SIGNAL y: BIT_VECTOR(7 DOWNTO 0);
  x <= '1';
  y <= "00000010";
  y <= (OTHERS => '0'); -- same as "00000000"

## Slide 11: STD_LOGIC and STD_LOGIC_VECTOR
The STD_LOGIC and STD_LOGIC_VECTOR types provide more values than the BIT type for modeling a real circuit more accurately. Objects of these types can have the following values.
  '0' − normal 0
  '1' − normal 1
  'Z' − high impedance
  '−' − don’t-care
  'L' − weak 0
  'H' − weak 1
  'U' − uninitialized
  'X' − unknown
  'W' − weak unknown

## Slide 12
The STD_LOGIC and STD_LOGIC_VECTOR types are not predefined, and so the following two library statements must be included in order to use these types.
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
If objects of type STD_LOGIC_VECTOR are to be used as binary numbers in arithmetic manipulations, then either one of the following two USE statements must also be included
  USE IEEE.STD_LOGIC_SIGNED.ALL;
  USE IEEE.STD_LOGIC_UNSIGNED.ALL;
for signed and unsigned number arithmetic
The predefined INTEGER type defines binary number objects for use with arithmetic operators. By default, an INTEGER signal uses 32 bits to represent a signed number. Integers using fewer bits can also be declared with the RANGE keyword.

## Slide 13
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
  SIGNAL x: STD_LOGIC;
  SIGNAL y: STD_LOGIC_VECTOR(7 DOWNTO 0);
  x <= 'Z';
  y <= "0000001Z";
  y <= (OTHERS => '0'); -- same as "00000000"
An enumeration type allows the user to specify the values that the data object can have.
Syntax:
  TYPE identifier IS (value1, value2, … );
Example:
  TYPE state_type IS (S1, S2, S3);
  SIGNAL state: state_type;
  state <= S1;

## Slide 14: ARRAY
The ARRAY type groups single data objects of the same type together into a one-dimensional or multidimensional array.
Syntax:
  TYPE identifier IS ARRAY (range) OF type;
Example:
  TYPE byte IS ARRAY(7 DOWNTO 0) OF BIT;
  TYPE memory_type IS ARRAY(1 TO 128) OF byte;
  SIGNAL memory: memory_type;
  memory(3) <= "00101101";

## Slide 15: SUBTYPE
A SUBTYPE is a subset of a type, that is, a type with a range constraint.
Syntax:
  SUBTYPE identifier IS type RANGE range;
Example:
  SUBTYPE integer4 IS INTEGER RANGE –8 TO 7;
  SUBTYPE cell IS STD_LOGIC_VECTOR(3 DOWNTO 0);
  TYPE memArray IS ARRAY(0 TO 15) OF cell;

## Slide 16: Data Operators

## Slide 17: ENTITY
An ENTITY declaration declares the external or user interface of the module similar to the declaration of a function. It specifies the name of the entity and its interface. The interface consists of the signals to be passed into the entity or out from it using the two keywords IN and OUT, respectively.
Syntax:
  ENTITY entity-name IS
  PORT (list-of-port-names-and-types);
  END entity-name;
Example:
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
  ENTITY Siren IS PORT (
  M: IN STD_LOGIC;
  D: IN STD_LOGIC;
  V: IN STD_LOGIC;
  S: OUT STD_LOGIC);
  END Siren;

## Slide 18: ARCHITECTURE
The ARCHITECTURE body defines the actual implementation of the functionality of the entity. This is similar to the definition or implementation of a function. The syntax for the architecture varies, depending on the model(dataflow, behavioral, or structural) you use.
Syntax: Dataflow model
  ARCHITECTURE architecture-name OF entity-name IS
  signal-declarations;
  BEGIN
  concurrent-statements;
  END architecture-name;
The concurrent statements are executed concurrently.

## Slide 19
Example:
  ARCHITECTURE Siren_Dataflow OF Siren IS
  SIGNAL term_1: STD_LOGIC;
  BEGIN
  term_1 <= D OR V;
  S <= term_1 AND M;
  END Siren_Dataflow;
Syntax: Behavioral model
  ARCHITECTURE architecture-name OF entity-name IS
    signal-declarations;
    function-definitions;
    procedure-definitions;
  BEGIN
    PROCESS-blocks;
    concurrent-statements;
    END architecture-name;
Statements within the PROCESS block are executed sequentially. However, the PROCESS block itself is a concurrent statement.

## Slide 20
Example:
  ARCHITECTURE Siren_Behavioral OF Siren IS
    SIGNAL term_1: STD_LOGIC;
  BEGIN
  PROCESS (D, V, M)
  BEGIN
  term_1 <= D OR V;
  S <= term_1 AND M;
  END PROCESS;
  END Siren_Behavioral;

## Slide 21: GENERIC
Generics allow information to be passed into an entity so that, for example, the size of a vector in the PORT list does not have to be known until elaboration time. Generics of an entity are declared with the GENERIC keyword before the PORT list declaration for the entity. An identifier that is declared as GENERIC is a constant that only can be read. The identifier then can be used in the entity declaration and its corresponding architectures wherever a constant is expected.
Syntax: In an ENTITY declaration
  ENTITY entity-name IS
  GENERIC (identifier: type); -- with no default value
  or
  ENTITY entity-name IS
  GENERIC (identifier: type := constant); -- with a default value given by the constant

## Slide 22
Example:
  ENTITY Adder IS
  -- declares the generic identifier n having a default value 4
  GENERIC (n: INTEGER := 4);
  PORT (
    -- the vector size is 3 downto 0 since n is 4
    A, B: IN STD_LOGIC_VECTOR(n-1 DOWNTO 0);
    Cout: OUT STD_LOGIC;
    SUM: OUT STD_LOGIC_VECTOR(n-1 DOWNTO 0));
    S: OUT STD_LOGIC);
  END Siren;

## Slide 23: PACKAGE
A PACKAGE provides a mechanism to group together and share declarations that are used by several entity units. A package itself includes a declaration and, optionally, a body. The PACKAGE declaration and body usually are stored together in a separate file from the rest of the design units. The file name given for this file must be the same as the package name. In order for the complete design to synthesize correctly using MAX+plus II, you must first synthesize the package as a separate unit. After that, you can synthesize the unit that uses that package.

## Slide 24: PACKAGE Declaration and Body
The PACKAGE declaration contains declarations that may be shared between different entity units. It provides the interface, that is, items that are visible to the other entity units. The optional PACKAGE BODY contains the implementations of the functions and procedures that are declared in the PACKAGE declaration.

## Slide 25
Example:
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
PACKAGE my_package IS
  SUBTYPE bit4 IS STD_LOGIC_VECTOR(3 DOWNTO 0);
  FUNCTION Shiftright (input: IN bit4) RETURN bit4; -- declare a function
  SIGNAL mysignal: bit4; -- a global signal
END my_package;
PACKAGE BODY my_package IS
  -- implementation of the Shiftright function
  FUNCTION Shiftright (input: IN bit4) RETURN bit4 IS
  BEGIN
RETURN '0' & input(3 DOWNTO 1);
END shiftright;
END my_package;

## Slide 26: Using a PACKAGE
To use a package, you simply include a LIBRARY and USE statement for that package. Before synthesizing the module that uses the package, you need to first synthesize the package by itself as a top-level entity.
LIBRARY WORK;
USE WORK.my_package.ALL;
ENTITY test_package IS PORT (
  x: IN bit4;
  z: OUT bit4);
END test_package;
ARCHITECTURE Behavioral OF test_package IS
BEGIN
  mysignal <= x;
  z <= Shiftright(mysignal);
END Behavioral;

## Slide 27: Concurrent Signal Assignment
The concurrent signal assignment statement assigns a value or the result of evaluating an expression to a signal. This statement is executed whenever a signal in its expression changes value. However, the actual assignment of the value to the signal takes place after a certain delay and not instantaneously as for variable assignments. The expression can be any logical or arithmetical expressions.
Syntax:
signal <= expression;
Example:
  y <= '1';
  z <= y AND (NOT x);

## Slide 28: Conditional Signal Assignment
The conditional signal assignment statement selects one of several different values to assign to a signal based on different conditions. This statement is executed whenever a signal in any one of the value or condition changes.
Syntax:
  signal <= value1 WHEN condition ELSE
  value2 WHEN condition ELSE
  z <= in0 WHEN sel = "00" ELSE
  in1 WHEN sel = "01" ELSE
  in2 WHEN sel = "10" ELSE
  in3;

## Slide 29: Selected Signal Assignment
The selected signal assignment statement selects one of several different values to assign to a signal based on the value of a select expression. All possible choices for the expression must be given. The keyword OTHERS can be used to denote all remaining choices. This statement is executed whenever a signal in the expression or any one of the value changes.
Example:
  WITH sel SELECT
  z <= in0 WHEN "00",
  in1 WHEN "01",
  in2 WHEN "10",
  in3 WHEN OTHERS;

## Slide 30
  -- outputs a 1 if the 4-bit input is a prime number, 0 otherwise
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
  ENTITY Prime IS PORT (
    number: IN STD_LOGIC_VECTOR(3 DOWNTO 0);
    yes: OUT STD_LOGIC);
  END Prime;
  ARCHITECTURE Prime_Dataflow OF Prime IS
  BEGIN
    WITH number SELECT
    yes <= '1' WHEN "0001" | "0010",
    '1' WHEN "0011" | "0101" | "0111" | "1011" | "1101",
    '0' WHEN OTHERS;
  END Prime_Dataflow;

## Slide 31: Behavioral Model Sequential Statements
The behavioral model allows statements to be executed sequentially just like in a regular computer program. Sequential statements include many of the standard constructs, such as variable assignments, if-then-else statements, and loops.
The PROCESS block contains statements that are executed sequentially. However, the PROCESS statement itself is a concurrent statement. Multiple process blocks in an architecture will be executed simultaneously. These process blocks can be combined together with other concurrent statements
Syntax:
  process-name: PROCESS (sensitivity-list)
  variable-declarations;
  BEGIN
  sequential-statements;
  END PROCESS process-name;

## Slide 32
The sensitivity list is a comma-separated list of signals, which the process is sensitive to. In other words, whenever a signal in the list changes value, the process will be executed (i.e., all of the statements in the sequential order listed). After the last statement has been executed, the process will be suspended until the next time that a signal in the sensitivity list changes value before it is executed again.
Example:
  PROCESS (D, V, M)
  BEGIN
    term_1 <= D OR V;
    S <= term_1 AND M;
  END PROCESS;

## Slide 33: Sequential Signal Assignment
The sequential signal assignment statement assigns a value to a signal. This statement is just like its concurrent counterpart, except that it is executed sequentially (i.e., only when execution reaches it).
Syntax:
  signal <= expression;
Example:
  y <= '1';
  z <= y AND (NOT x);

## Slide 34: Variable Assignment
The variable assignment statement assigns a value or the result of evaluating an expression to a variable. The value is always assigned to the variable instantaneously whenever this statement is executed.
Variables are only declared within a process block.
Syntax:
  signal := expression;
Example:
  y := '1';
  yn := NOT y;

## Slide 35: WAIT
When a process has a sensitivity list, the process always suspends after executing the last statement. An alternative to using a sensitivity list to suspend a process is to use a WAIT statement, which must also be the first statement in a process.
Syntax:
  WAIT UNTIL condition;
Example:
  -- suspend until a rising clock edge
  WAIT UNTIL clock’EVENT AND clock = '1';

## Slide 36: IF THEN ELSE
Syntax:
  IF condition THEN
  sequential-statements1;
  ELSE
  sequential-statements2;
  END IF;
  IF condition1 THEN
  sequential-statements1;
  ELSIF condition2 THEN
  sequential-statements2;
  …
  ELSE
  sequential-statements3;
  END IF;
Example:
  IF count /= 10 THEN -- not equal
  count := count + 1;
  ELSE
  count := 0;
  END IF;

## Slide 37: CASE
Syntax:
  CASE expression IS
  WHEN choices => sequential-statements;
  WHEN choices => sequential-statements;
  …
  WHEN OTHERS => sequential-statements;
  END CASE;
Example:
  CASE sel IS
  WHEN "00" => z <= in0;
  WHEN "01" => z <= in1;
  WHEN "10" => z <= in2;
  WHEN OTHERS => z <= in3;
  END CASE;

## Slide 38: FOR
Syntax:
  FOR identifier IN start [TO | DOWNTO] stop LOOP
  sequential-statements;
  END LOOP;
  Loop statements must have locally static bounds7. The identifier is implicitly declared, so no explicit declaration
  of the variable is needed.
Example:
  sum := 0;
  FOR count IN 1 TO 10 LOOP
  sum := sum + count;
  END LOOP;

## Slide 39: NEXT
The NEXT statement can be used only inside a loop. It causes execution to skip to the end of the current iteration and continue with the beginning of the next iteration. It is usually used in conjunction with the FOR statement.
Syntax:
  NEXT WHEN condition;
Example:
  sum := 0;
  FOR count IN 1 TO 10 LOOP
  NEXT WHEN count = 3;
  sum := sum + count;
  END LOOP;

## Slide 40: FUNCTION
Syntax: Function declaration
  FUNCTION function-name (parameter-list) RETURN return-type;
Syntax: Function definition
  FUNCTION function-name (parameter-list) RETURN return-type IS
  BEGIN
  sequential-statements;
  END function-name;
Syntax: Function call
  function-name (actuals);
  Parameters in the parameter list can be either signals or variables of mode IN only.

## Slide 41
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
  ENTITY test_function IS PORT (
    x: IN STD_LOGIC_VECTOR(3 DOWNTO 0);
    z: OUT STD_LOGIC_VECTOR(3 DOWNTO 0));
  END test_function;
  ARCHITECTURE Behavioral OF test_function IS
    SUBTYPE bit4 IS STD_LOGIC_VECTOR(3 DOWNTO 0);
    FUNCTION Shiftright (input: IN bit4) RETURN bit4 IS
    BEGIN
    RETURN '0' & input(3 DOWNTO 1);
    END shiftright;
    SIGNAL mysignal: bit4;
  BEGIN
    PROCESS
    BEGIN
    mysignal <= x;
    z <= Shiftright(mysignal);
    END PROCESS;
  END Behavioral;

## Slide 42: Behavioral Model Sample
  LIBRARY IEEE;
  USE IEEE.STD_LOGIC_1164.ALL;
  ENTITY bcd IS PORT (
    I: IN STD_LOGIC_VECTOR(3 DOWNTO 0);
    Segs: OUT STD_LOGIC_VECTOR(1 TO 7));
  END bcd;
  ARCHITECTURE Behavioral OF bcd IS
  BEGIN
    PROCESS(I)
    BEGIN
    CASE I IS
    WHEN "0000" => Segs <= "1111110";
    WHEN "0001" => Segs <= "0110000";
    WHEN "0010" => Segs <= "1101101";
    WHEN "0011" => Segs <= "1111001";
    WHEN "0100" => Segs <= "0110011";
    WHEN "0101" => Segs <= "1011011";
    WHEN "0110" => Segs <= "1011111";
    WHEN "0111" => Segs <= "1110000";
    WHEN "1000" => Segs <= "1111111";
    WHEN "1001" => Segs <= "1110011";
    WHEN OTHERS => Segs <= "0000000";
    END CASE;
    END PROCESS;
  END Behavioral;

## Slide 43
End of Lecture 5
Thank you for your attention!