## Slide 1: EEE3131 Digital Electronics
Lecture 6 : IC Technologies
Instructor: George ZIBA
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Email: george.ziba@unza.zm
0976854627

## Slide 2: Introduction
Digital integrated circuits are produced using several different circuit configurations and production technologies.
Each such approach is called a specific logic family.
The idea is that different logic functions, when fabricated in the form of an IC with the same approach, or in other words belonging to the same logic family, will have identical electrical characteristics.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
2
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
3
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 3
These characteristics include supply voltage range, speed of response, power dissipation, input and output logic levels, current sourcing and sinking capability, fan-out, noise margin, etc.
In other words, the set of digital ICs belonging to the same logic family are electrically compatible with each other
The entire range of digital ICs is fabricated using either bipolar devices or MOS devices or a combination of the two.
Different logic families falling in the first category are called bipolar families.
3
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 4
These include diode logic (DL), resistor transistor logic (RTL), diode transistor logic (DTL), transistor transistor logic (TTL), emitter coupled logic (ECL), also known as current mode logic (CML), and integrated injection logic (I2L).
The logic families that use MOS devices as their basis are known as MOS families, and the prominent members belonging to this category are the PMOS family(using P-channel MOSFETs), the NMOS family (using N-channel MOSFETs) and the CMOS family(using both N- and P-channel devices).
The Bi-MOS logic family uses both bipolar and MOS devices.
4
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 5
Diodes and resistors in fact were never implemented in integrated circuits.
Both RTL and DTL suffered from large propagation delay owing to the need for the transistor base charge to leak out if the transistor were to switch from conducting to non-conducting state.
Logic families that are still in widespread use include TTL, CMOS, ECL, NMOS, Bi-CMOS, PMOS and I2L.
Those logic circuits in which transistors are driven into saturation are called saturated logic circuits or simply saturated logic. Those circuits which avoid saturation of their transistors are called non-saturated logic.
5
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 6: advantages of using ICs
Reduction of the overall size of the digital circuit.
Reduction of the cost because of mass-producing volume of similar ICs.
Lower power consumption because of extremely small size of logic circuits.
Increased reliability because of reduced external interconnections from one device to another
6
7
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Obviously, saturated logic circuits have low switching speeds whereas non-saturated type are much faster. TTL is the example of a saturated logic whereas ECL represents a non-saturated logic.

## Slide 7: Characteristic Parameters
HIGH-level input current, IIH. This is the maximum current flowing into (taken as positive) or out of (taken as negative) an input when a HIGH-level input voltage equal to the minimum HIGH-level output voltage specified for the family is applied.
LOW-level input current, IIL. The LOW-level input current is the maximum current flowing into(taken as positive) or out of (taken as negative) the input of a logic function when the voltage applied at the input equals the maximum LOW-level output voltage specified for the family.
7
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 8
HIGH-level output current, IOH. This is the maximum current flowing out of an output when the input conditions are such that the output is in the logic HIGH state.
It tells about the current sourcing capability of the output. The magnitude of IOH determines the number of inputs the logic function can drive when its output is in the logic HIGH state.
LOW-level output current, IOL. This is the maximum current flowing into the output pin of a logic function when the input conditions are such that the output is in the logic LOW state.
It tells about the current sinking capability of the output. The magnitude of IOL determines the number of inputs the logic function can drive when its output is in the logic LOW state
8
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 9
9
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.1: Input and output current specifications

## Slide 10
HIGH-level input voltage, VIH. This is the minimum voltage level that needs to be applied at the input to be recognized as a legal HIGH level for the specified family.
For the standard TTL family, a 2 V input voltage is a legal HIGH logic state
LOW-level input voltage, VIL. This is the maximum voltage level applied at the input that is recognized as a legal LOW level for the specified family.
For the standard TTL family, an input voltage of 0.8 V is a legal LOW logic state.
10
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 11
HIGH-level output voltage, VOH. This is the minimum voltage on the output pin of a logic function when the input conditions establish logic HIGH at the output for the specified family.
In the case of the standard TTL family of devices, the HIGH level output voltage can be as low as 2.4V and still be treated as a legal HIGH logic state.
It may be mentioned here that, for a given logic family, the VOH specification is always greater than the VIH specification to ensure output-to-input compatibility when the output of one device feeds the input of another.
11
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 12
LOW-level output voltage, VOL. This is the maximum voltage on the output pin of a logic function when the input conditions establish logic LOW at the output for the specified family.
In the case of the standard TTL family of devices, the LOW-level output voltage can be as high as 0.4V and still be treated as a legal LOW logic state.
It may be mentioned here that, for a given logic family, the VOL specification is always smaller than the VIL specification to ensure output-to-input compatibility when the output of one device feeds the input of another.
12
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 13
13
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.2: (a) HIGH-level current and voltage parameters and
(b) LOW-level current and voltage parameters

## Slide 14
Supply current, ICC. The supply current when the output is HIGH and LOW is respectively designated as ICCH, ICCL
Rise time, tr. This is the time that elapses between 10 and 90 % of the final signal level when the signal is making a transition from logic LOW to logic HIGH.
Fall time, tf . This is the time that elapses between 90 and 10 % of the signal level when it is making a HIGH to LOW transition.
Propagation delay tp. The propagation delay is the time delay between the occurrence of change in the logical level at the input and before it is reflected at the output. It is the time delay between the specified voltage points on the input and output waveforms.
14
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 15
Propagation delay tpLH. This is the time delay between specified voltage points on the input and output waveforms with the output changing from LOW to HIGH.
Propagation delay tpHL. This is the time delay between specified voltage points on the input and output waveforms with the output changing from HIGH to LOW.
DC Supply Voltage. The standard value of the dc supply voltage for TTL (i.e., transistor-transistor logic) and CMOS (i.e., complementary metal-oxide semiconductor) device is + 5V.
15
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 16
16
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.3: Propagation delay parameters.

## Slide 17
Power dissipation. The power dissipation parameter for a logic family is specified in terms of power consumption per gate and is the product of supply voltage VCC and supply current ICC. The supply current is taken as the average of the HIGH-level supply current ICCH and the LOW-level supply current ICCL.
Speed–power product. The speed of a logic circuit can be increased, that is, the propagation delay can be reduced, at the expense of power dissipation. It is always desirable to have in a logic family low values for both propagation delay and power dissipation parameters. A useful figure-of-merit used to evaluate different logic families is the speed–power product, expressed in picojoules
17
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 18
Fan-out. The fan-out is the number of inputs of a logic function that can be driven from a single output without causing any false output. It is a characteristic of the logic family to which the device belongs. It can be computed from IOH/IIH in the logic HIGH state and from IOL/IIL in the logic LOW state. If, in a certain case, the two values are different, the fan-out is taken as the smaller of the two.
Noise Margin (NM) of a gate is the maximum noise voltage that can be added to an input signal without causing undesirable outputs.
Noise comes in form of DC noise caused by voltage level drift and also from AC noise caused by random pauses of other switching circuits etc. Noise margin is calculated using voltage levels of the input signal and output signal.
18
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 19
19
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.4: Noise Margin (NM)

## Slide 20: Example
A TTL logic gate draws 2 mA when its output is HIGH and 3.5 mA when its output is LOW. Calculate the average power dissipation if the supply voltage is 5 V and the logic gate is operated on 50% duty cycle.
20
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 22: DL, RTL and DTL Circuits
22
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
DL Characteristics
Used diodes and resistors
Was never implemented
Only has historical significance
Figure 6.5: DL Circuit

## Slide 23
23
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.6: DTL and RTL Circuits

## Slide 24: Transistor Transistor Logic (TTL)
TTL as outlined above stands for transistor transistor logic. It is a logic family implemented with bipolar process technology that combines or integrates NPN transistors, PN junction diodes and diffused resistors in a single monolithic structure to get the desired logic function.
It is a saturated logic. It is the most widely used circuit line since early 1970s because of its speed, good fan-out and easy interface with other digital circuitry.
The unique feature of this circuit is that it used multiple-emitter transistor at input which replaces the input diodes of the DTL
24
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 25
The number of emitters is equal to the number of inputs of the logic circuit (limited to 8)
Since a multi-emitter transistor is small in area than the diodes it replaces, the yield from a wafer is increased
Moreover, smaller area results in lower capacitance to the substrate, thereby wide selection of circuit modules ranging from simple gates and flip-flops in SSI circuit series through various registers in computers in MSI circuit series to micro-processor bit-slice chips in the LSI series
25
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 26: Basic Circuit of TTL
26
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.7: TTL NAND Gate Circuit

## Slide 27: Circuit Operation
When either of the two inputs or both inputs are in the logic LOW state, the base-emitter region of Q1 conducts current, driving Q2 to cut-off in the process. When Q2 is in the cut-off state, Q3 is driven to conduction and Q4 to cut-off. This produces a logic HIGH output with VOH (min) = 2.4 V guaranteed for minimum supply voltage Vcc and a source current of 400 uA.
When both the inputs are in the logic HIGH state as specified by the TTL family, the current flows through the base-collector PN junction diode of transistor Q1 into the base of transistor Q2. Transistor Q2 is turned ON to saturation, with the result that transistor Q3 is switched OFF and transistor Q4 is switched ON. This produces a logic LOW at the output, with VOL being 0.4 V maximum when it is sinking a current of 16 mA from external loads represented by inputs of logic functions being driven by the output.
28

## Slide 28: TTL NAND Key Features
The multi-emitter input transistor is a special design such that each emitter acts like a diode. This makes Q1 and the 4K resistor to act like an AND gate. This kind of transistor requires less area on the silicon wafer during fabrication and therefore results in relatively faster speeds of operation.
The Totem-pole has advantage of low output impedance either as Emitter follower or as Ground and therefore low time constants when connecting to the next stage
The Diode D1 ensures that Q3 does not conduct when output is low. Its voltage keeps the base-emitter diode of Q3 in reverse biased mode
28
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 29: Standard TTL Characteristics
greater speed than DTL,
low noise immunity (0.4 V),
average propagation delay per gate of 9 ns,
average power dissipation of 10 mW,
a fan-out of 10 meaning one output can drive 10 other TTL inputs,
29
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 30: TTL Sub-families
Two versions of TTL identified by the following series numbers:
5400 series: Military version, -55o C to 125o C.
7400 series: Commercial version, , 0o C to 70o C
5400 series devices can replace 7400s but cost too high.
We will now give a bit more detailed description of various configurations of the TTL 7400 series that are used in order to optimize between power usage, switching speeds, etc.
30
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 31
74L00 series — the letter L standing for low power consumption. It has an average power dissipation of 1 mW per gate but an average propagation delay of 33 ns.
The circuit is the same as that of the standard TTL NAND gate except for an increased resistance value of the different resistors used in the circuit.
74H00 series — the letter H standing for higher speed. It has a propagation delay of 6 ns but average power dissipation of 23 mW/gate.
The circuit is the same as that of the standard TTL NAND gate except for transistors Q3 and diode D1 combination in the totem-pole output stage having been replaced by a Darlington arrangement
31
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 32
74S00 — the letter S representing Schottky. It has the highest speed because its average propagation delay is just 3 ns per gate. However, its average power dissipation is 23 mW/gate.
The circuit is the same as that of the standard TTL NAND gate except all the transistors are replaced with Schottky transistors
A Schottky transistor is nothing but a conventional bipolar transistor with a Schottky diode connected between its base and collector terminals.
The presence of a Schottky diode does not allow the transistor to go to deep saturation
32
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 33
74LS00 — It is called low-power Schottky TTL. It has an average propagation delay of 9.5 ns and an average power dissipation of 2 mW.
74AS00 series — The letter A representing Advanced and S standing for schottky. It is called advanced schottky TTL series. It is the fastest TTL series.
74ALS00 series — It is called Advanced Low-power Schottky TTL series. The 74ALS series has the lower speed-power product and the lowest gate power dissipation of all the TTL series.
33
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 34: Emitter Coupled Logic (ECL)
The ECL family is the fastest logic family in the group of bipolar logic families. The characteristic features that give this logic family its high speed or short propagation delay are outlined as follows:
It is a non-saturating logic. That is, the transistors in this logic are always operated in the active region of their output characteristics. They are never driven to either cut-off or saturation, which means that logic LOW and HIGH states correspond to different states of conduction of various bipolar transistors.
34
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 35
The logic swing, that is, the difference in the voltage levels corresponding to logic LOW and HIGH states, is kept small (typically 0.85 V), with the result that the output capacitance needs to be charged and discharged by a relatively much smaller voltage differential.
The circuit currents are relatively high and the output impedance is low, with the result that the output capacitance can be charged and discharged quickly
35
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 36: ECL Circuit
36
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.8: ECL OR/NOR Gate Circuit

## Slide 37: ECL Characteristics
propagation delay time per gate of 0.3 ns (meaning extremely fast speed),
power dissipation of 25 mW,
fan-out of 25 to 50,
noise margin from about 0.2 to 0.25 V.
37
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 38: The CMOS Family
The CMOS (Complementary Metal Oxide Semiconductor) logic family uses both N-type and P-type MOSFETs to realize different logic functions.
The main advantage of the CMOS logic family over bipolar logic families discussed so far lies in its extremely low power dissipation, which is near-zero in static conditions.
In fact, CMOS devices draw power only when they are switching. This allows integration of a much larger number of CMOS gates on a chip than would have been possible with bipolar or NMOS technology. CMOS technology today is the dominant semiconductor technology used for making microprocessors, memory devices and application-specific integrated circuits (ASICs).
38
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 39
The input to a MOSFET is electrically isolated from the rest of the MOSFET which reduces the input current and power dissipation.
Using an N-channel MOSFET with its complement, the P-channel MOSFET, a simple complementary MOS (CMOS) inverter can be formed, as shown in the next slide.
39
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 40
40
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6.9: CMOS inverter formed from complementary
N-channel/P-channel transistors.

## Slide 41
41
42
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.0: Naming and evolution of CMOS family .

## Slide 42
End of Lecture 6
Thank you for your attention!