## Slide 1: EEE3131 Digital Electronics
Lecture 7 : Combinational Logic Circuits
Instructor: George ZIBA
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Email: george.ziba@unza.zm
0976854627

## Slide 2: Introduction
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
A combinational logic circuit is one where the output or outputs depend upon the present state of combination of the logic inputs
A combinational circuit is one where the output at any time depends only on the present combination of inputs at that point of time with total disregard to the past state of the inputs.
The logic gate is the most basic building block of combinational logic.
The logical function performed by a combinational circuit is fully defined by a set of Boolean expressions.

## Slide 3
Introduction
2
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Combinational logic functions and many more, including more complex ones, are available in monolithic IC form.
In combinational circuits, input variables come from an external source and output variables feed an external destination.

## Slide 4
Introduction
3
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.1: Combinational circuit with normal and complemented inputs.

## Slide 5
Introduction
4
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
The different steps involved in the design of a combinational logic circuit are as follows:
Statement of the problem.
Identification of input and output variables.
Expressing the relationship between the input and output variables.
Construction of a truth table to meet input–output requirements.
Writing Boolean expressions for various output variables in terms of input variables.
Minimization of Boolean expressions.
Implementation of minimized Boolean expressions.

## Slide 6
Introduction
5
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
There are various possible minimized forms of Boolean expressions. The following guidelines should be followed while choosing the preferred form for hardware implementation
The implementation should have the minimum number of gates, with the gates used having the minimum number of inputs.
There should be a minimum number of interconnections, and the propagation time should be the shortest.
Limitation on the driving capability of the gates should not be ignored.

## Slide 7
Hexadecimal Arithmetic
6
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Hexadecimal representation is a method of representing groups of 4 bits as a single digit.
Hexadecimal notation has been widely adopted by manufacturers of computers and microprocessors because it simplifies the documentation and use of their equipment.
Eight- and 16-bit computer system data, program instructions, and addresses use hexadecimal to make them easier to interpret and work with than their binary equivalents.

## Slide 8
7
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Hexadecimal Arithmetic
Figure 7.2: Hexadecimal Digits with Their Equivalent Binary and Decimal Values

## Slide 9
8
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Hexadecimal Arithmetic
The procedure for adding hex digits is as follows:
Add the two hex digits by working with their decimal equivalents.
If the decimal sum is less than 16, write down the hex equivalent.
If the decimal sum is 16 or more, subtract 16, write down the hex result in that column, and carry 1 to the next-more-significant column.

## Slide 10
Examples
9
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 11
BCD Arithmetic
10
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Digital electronics naturally work in binary, and we have to group four binary digits together to get enough combinations to represent the 10 different decimal digits.
This 4-bit code is called binary-coded decimal (BCD).
So what we have is a 4-bit code that is used to represent the decimal digits that we need when reading a display on calculators or computer output.

## Slide 12
11
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
BCD Arithmetic
The procedure for BCD addition is as follows:
Add the BCD numbers as regular true binary numbers.
If the sum is 9 (1001) or less, it is a valid BCD answer; leave it as is.
If the sum is greater than 9 or there is a carry-out of the MSB, it is an invalid BCD number; do step 4.
If it is invalid, add 6 (0110) to the result to make it valid. Any carry-out of the MSB is added to the next-more-significant BCD number.
Repeat steps 1 to 4 for each group of BCD bits.

## Slide 13
12
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Examples
Convert the following decimal numbers to BCD and add them. Convert the result back to decimal to check your answer.
8 + 7
9 + 9
52 + 63
78 + 69

## Slide 14
13
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 15
14
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Arithmetic Circuits – Basic Building Blocks
Addition and subtraction are the two most commonly used arithmetic operations, as the other two, namely multiplication and division, are respectively the processes of repeated addition and repeated subtraction

## Slide 16
16
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Half-Adder
A half-adder is an arithmetic circuit block that can be used to add two bits.
Such a circuit thus has two inputs that represent the two bits to be added and two outputs, with one producing the SUM output and the other producing the CARRY.
Figure 7.3: Half adder and its truth table

## Slide 17
17
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Half-Adder
The Boolean expressions for the SUM and CARRY outputs are given by the equations:

## Slide 18
18
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Half-Adder
Figure 7.4: Logic implementation of a half-adder.

## Slide 19
19
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Full Adder
A full adder circuit is an arithmetic circuit block that can be used to add three bits to produce a SUM and a CARRY output.
The full adder circuit overcomes the limitation of the half-adder, which can be used to add two bits only
A full adder is therefore essential for the hardware implementation of an adder circuit capable of adding larger binary numbers. A half-adder can be used for addition of LSBs only.

## Slide 20
Full Adder
20
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.5: Full Adder and its truth table

## Slide 21
21
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Full Adder
Figure 7.6: Full Adder Circuit

## Slide 22
22
22
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Full Adder
Figure 7.7: Full Adder Circuit

## Slide 23
23
23
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.8: Full Adder Circuit from half adders
Full Adder

## Slide 24
24
24
24
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.9: Four bit binary adder
Full Adder

## Slide 25: VHDL Code for a Full Adder
Library ieee;
use ieee.std_logic_1164.all;
entity full_adder is
port(a,b,c :in bit;
sum,carry :out bit);
end full_adder;
architecture data of full_adder is
begin
sum<= a xor b xor c;
carry <= ((a and b) or (b and c) or (a and c));
end data;

## Slide 26
26
26
26
26
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.10: Four bit adder ICs
Four-Bit Full-Adder ICs

## Slide 27
27
27
27
27
27
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.11: 4-bit adder ICs to form an 8-bit adder
Four-Bit Full-Adder ICs

## Slide 28
28
28
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Half-Subtractor
Figure 7.12: Half Subtractor circuit and truth table

## Slide 29
29
29
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Full Subtractor
Figure 7.13: Full Subtractor and its truth table

## Slide 30
30
30
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Full Subtractor
Figure 7.14: Full Subtractor Circuit

## Slide 31
31
31
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Controlled Inverter
A controlled inverter is needed when an adder is to be used as a subtractor. As outlined earlier, subtraction is nothing but addition of the 2’s complement of the subtrahend to the minuend.
Thus, the first step towards practical implementation of a subtractor is to determine the 2’s complement of the subtrahend.
And for this, one needs firstly to find 1’s complement. A controlled inverter is used to find 1’s complement.
Full adders can be used to perform subtraction provided we have the necessary additional hardware to generate 2’s complement of the subtrahend and disregard the final carry or overflow.

## Slide 32
32
32
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Adder–Subtractor
Figure 7.15: Adder-Subtractor

## Slide 33
33
33
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Adder–Subtractor
Figure 7.16: 8-bit adder subtractor using ICs

## Slide 34
34
34
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
BCD Adder Circuit
BCD adders can also be formed using the IC 4-bit binary adders. The problem is that when any group-of-four BCD sum exceeds 9, or when there is a carry-out, the number is invalid and must be corrected by adding 6 to the invalid answer to get the correct BCD answer.
Checking for a sum greater than 9, or a carry-out, can be done easily using logic gates. Then, when an invalid sum occurs, it can be corrected by adding 6.
A 4-bit BCD adder is available in a single IC package. The 74HCT583 IC has internal correction circuitry to add two 4-bit numbers and produce a corrected 4-bit answer with carry-out.

## Slide 35
35
35
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
BCD Adder Circuit
Figure 7.17: BCD adder using ICs

## Slide 36
36
36
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Binary Multiplier Circuit
The multiplication of binary numbers is done the same way as in decimal multiplication. To see how a binary multiplier works let us consider the two 2-bit binary numbers: A0 A1 and Bo B1

## Slide 37
37
37
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Binary Multiplier Circuit
Figure 7.18: 4-bit multipliers using ICs

## Slide 38
38
Arithmetic/Logic Units
Arithmetic/logic units (ALUs) are available in large-scale IC packages (LSI). The LSI circuits are generally considered to be ICs containing from 100 to 10,000 gate equivalents.
Typically, an ALU is a multipurpose device capable of providing several different arithmetic and logic operations.
The specific operation to be performed is chosen by the user by placing a specific binary code on the mode select inputs.
Microprocessors may also have ALUs built in as one of their many operational units. In such cases, the specific operation to be performed is chosen by software instructions.
38
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 39
39
39
Arithmetic/Logic Units
39
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Once the mode control (M) is set, you have 16 choices within either the logic or arithmetic categories. The specific function you want is selected by applying the appropriate binary code to the function select inputs (S3 to S0).
Figure 7.19: Arithmetic and Logic Unit

## Slide 40
40
40
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Magnitude Comparator
A magnitude comparator is a combinational circuit that compares two given numbers and determines whether one is equal to, less than or greater than the other.
In order to determine whether A is greater than or less than B we inspect the relative magnitude of pairs of significant digits, starting from the most significant position. The comparison is done by successively comparing the next adjacent lower pair of digits if the digits of the pair under examination are equal.

## Slide 41
41
41
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Magnitude Comparator
Figure 7.20: Magnitude Comparator with truth table

## Slide 42
42
42
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
4-bit Magnitude Comparator
To determine whether A is greater or less than B. We consider the relative magnitude of pairs of significant digits starting from the MSB position. If the two digits are equal then we compare the next lower significant pair of digits.
The comparison follows until a pair of unequal digits are reached. If the corresponding digit of A is 1 and that of B is 0, then A > B. If the corresponding digit A is 0 and that of B is 1, then A < B. This discussion can be expressed logically as:

## Slide 43
43
43
43
43
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
4-bit Magnitude Comparator
The logic diagram of 4-bit comparator is shown in the next slide. The four output X0, X1, X2 and X3 are generated with Ex-NOR gates are applied to an AND gate (Gate 1). It gives the output binary A = B. The OR gate (Gate 2) gives the output binary A > B and the OR gate (Gate 3) gives the output binary A < B.

## Slide 44
44
44
44
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
4-bit Magnitude Comparator
Figure 7.21: 4-bit comparator and its IC

## Slide 45
45
44
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Multiplexer
A multiplexer or MUX, also called a data selector, is a combinational circuit with more than one input line, one output line and more than one selection line.
There are some multiplexer ICs that provide complementary outputs. Also, multiplexers in IC form almost invariably have an ENABLE or STROBE input, which needs to be active for the multiplexer to be able to perform its intended function.

## Slide 46
46
46
46
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Multiplexer
A multiplexer selects binary information present on any one of the input lines, depending upon the logic status of the selection inputs, and routes it to the output line.
If there are n selection lines, then the number of maximum possible input lines is 2n and the multiplexer is referred to as a 2n -to-1 multiplexer or 2n ×1 multiplexer.

## Slide 47
47
47
47
47
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Multiplexer
Figure 7.22: Multiplexer circuit and truth table

## Slide 48: VHDL Code for a Multiplexer
Library ieee;
use ieee.std_logic_1164.all;
entity mux is
port(A,B,D0,D1,D2,D3:in bit; Y:out bit);
end mux;
architecture data of mux is
begin
Y<= (not S0 and not S1 and D0) or
(S0 and not S1 and D1) or
(not S0 and S1 and D2) or
(S0 and S1 and D3);
end data;

## Slide 49
49
Multiplexer
49
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 50
50
50
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Encoders
An encoder is a multiplexer without its single output line. It is a combinational logic function that has 2n (or fewer) input lines and n output lines, which correspond to n selection lines in a multiplexer.
The n output lines generate the binary code for the possible 2n input lines. Let us take the case of an octal-to-binary encoder. Such an encoder would have eight input lines, each representing an octal digit, and three output lines representing the three-bit binary equivalent.
A good example is a keyboard where a binary code should be generated for every key stroke.

## Slide 51
51
51
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Encoders
Figure 7.23: 4-bit encoder and truth table

## Slide 52
52
52
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Priority Encoder
A priority encoder is a practical form of an encoder. The encoders available in IC form are all priority encoders. In this type of encoder, a priority is assigned to each input so that, when more than one input is simultaneously active, the input with the highest priority is encoded.
Figure 7.24: priority encoder truth table

## Slide 53
53
Demultiplexers and Decoders
53
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
A demultiplexer is a combinational logic circuit with an input line, 2n output lines and n select lines. It routes the information present on the input line to any of the output lines.
The output line that gets the information present on the input line is decided by the bit status of the selection lines.
A decoder is a special case of a demultiplexer without the input line.
A decoder, is a combinational circuit that decodes the information on n input lines to a maximum of 2n unique output lines.

## Slide 54
54
54
Demultiplexers and Decoders
54
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.25: Demultiplexer truth table and decoder

## Slide 55
55
55
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Demultiplexers and Decoders
Figure 7.26: Decoder and truth table

## Slide 56: VHDL Code for a 3 x 8 Decoder
library ieee;
use ieee.std_logic_1164.all;
entity dec is
port(A,B,C:in bit; Y0,Y1,Y2,Y3,Y4,Y5,Y6,Y7: out bit);
end dec;
architecture vcgandhi of dec is
begin
Y0<=(not A) and (not B) and (not C);
Y1<=(not A) and (not B) and C;
Y2<=(not A) and B and (not C);
Y3<=(not A) and B and C;
Y4<=A and (not B) and (not C);
Y5<=A and (not B) and C;
Y6<=A and B and (not C);
Y7<=A and B and C;
end vcgandhi;

## Slide 57
57
Code Converters
57
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
The availability of large different types of codes for the same discrete elements of information result in the use of different codes by different digital systems.
Sometimes, it may happen that the use of output of one number system as the input to another number system. Hence it is necessary to design a conversion circuit and insert it between the two systems.
A code converter is a circuit, which accepts the input information in one binary code, converts it and produces an output into another binary code i.e., which makes the two systems compatible, even though each uses a different binary code.

## Slide 58
58
BCD-to-Seven-Segment Converters
58
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Calculators and other devices with numeric displays use another form of code conversion involving BCD-to-seven-segment conversion.
The term seven segment comes from the fact that these displays utilize seven different illuminating segments to make up each of the 10 possible numeric digits.
A code converter must be employed to convert the 4-bit BCD into a 7-bit code to drive each digit. A commonly used BCD-to seven-segment converter is the 7447 IC.

## Slide 59
59
59
BCD-to-Seven-Segment Converters
59
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.29: Wiring of decoder and seven-segment LED display

## Slide 60
60
60
60
Gray Code
60
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7.30: binary/gray to gray/binary converter

## Slide 61
End of Lecture 7
Thank you for your attention!