## Slide 1: Digital Electronics
Memories

## Slide 2: Objectives
At the end of the lecture students should be able:
  To know Terminology associated with memory systems.
  Steps that occur when the CPU reads from or writes to memory.
  Various types of memories & common applications.
  Organization/operation of static and dynamic RAMs.

## Slide 3: Introduction
Virtually any digital system requires some kind of memory, hence it is important to understand how memories are built, their main features, and how they work.

## Slide 4: Memory Termilogy
Digital data can be stored as charges on capacitors.
  An important semiconductor memory type does this for high-density storage, at low power-requirements.

## Slide 5: Continue
Semiconductor memories are used as the main memory of a computer where fast operation is important.
RAM and ROM make up main memory.
A computer’s main memory—its working memory—is in constant communication with the central processing unit (CPU) as a program of instructions is executed.

## Slide 6: Continue
Another form of storage is performed by auxiliary memory, separate from the main memory.
Common auxiliary memory devices are magnetic disk and compact disc (CD), accessed optically.
Also called mass storage—it has the capacity to store massive amounts of data without need for power.

## Slide 7: Continue
Memory Cell—a device or an electrical circuit used to store a single bit (0 or 1).
  Examples include a flip-flop, charged capacitor, or a single spot on magnetic tape or disk.
Memory Word—a group of bits (cells) in a memory that represents instructions or data.
  Word sizes in computers typically range from 8 to 64 bits, depending on the size of the computer.
Byte—a special term used for a group of eight bits.
  Always consists of eight bits.
Capacity—a way of specifying how many bits can be stored in a memory device or system.

## Slide 8: Continue
Density—another term for capacity.
  A memory device with greater density can store more bits in a given amount of space.
Address—a number that identifies the location of a word in memory.
  Addresses always exist in a digital system as a binary number, although octal, hex & decimal numbers are often used to represent the address for convenience.

## Slide 9: Continue
A small memory consisting of eight words.
Each of these eight words has a specific address represented as a three-bit number—from 000 to 111.
To refer to a specific word location in memory, use its address code to identify it.

## Slide 10: Continue
Read Operation—the binary word stored in a specific memory location (address) is sensed and then transferred to another device.
  Often called a fetch operation because a word is being fetched from memory.
Write Operation—operation whereby a new word is placed into a particular memory location.
  Also referred to as a store operation, it replaces the word that was previously stored there.
Access Time—measure of memory device speed, it is the time between the memory receiving a new address input & data is available at the output.

## Slide 11: Continue
Volatile Memory—any memory that requires the application of electrical power to store information.
  If the electrical power is removed, all information stored in the memory will be lost.
Random-Access Memory (RAM)—memory in which actual physical location of a memory word has no effect on how long it takes to read from, or write into, that location.
  Access time is the same for any address in memory.
    Most semiconductor memories are RAMs.

## Slide 12: Continue
Sequential-Access Memory (SAM)—type of memory in which the access time is not constant but varies depending on the address location.
  A stored word is found by sequencing through all address locations until the desired address is reached.
    Access times far longer than random-access memory.
Read/Write Memory (RWM)—any memory that can be read from or written into with equal ease.
Read-Only Memory (ROM)—broad class of semiconductor memories designed for applications with a high ratio of read- to write- operations.

## Slide 13: Continue
Static Memory Devices—semiconductor memory devices in which stored data remains permanently stored as long as power is applied.
  Without need for periodically rewriting data to memory.
Dynamic Memory Devices—semiconductor memory in which stored data will not remain permanently stored, even with power applied.
  Unless the data are periodically rewritten into memory.
    A refresh operation.
Main Memory—a computer’s working memory.
  Stores instructions and data the CPU is currently working on.

## Slide 14: Continue
Cache Memory—high-speed block of memory that operates between slower main memory and the CPU to optimize the speed of the computer.
  Physically located in the CPU, mother board, or both.
Auxiliary Memory—referred to as mass storage because it stores massive amounts of information external to the main memory.
  Slower than main memory, always nonvolatile.

## Slide 15: General Memory Operation
Every memory system requires I/O lines to:
  Apply the binary address of the memory location that is to be accessed.
  Enable memory devices to respond to control inputs.
  Place data stored in the specified address.
  In a read operation, enable the tristate outputs.
    Which applies the data to the output pins.
  In a write operation, apply the data to be stored to the data input pins.
  Enable the write operation, which causes the data to be stored at the specified location.
  Deactivate the read or write controls when done reading or writing and disable the memory IC.

## Slide 16: General Memory Operation
Diagram of a 32 x 4 memory, and the virtual arrangement of memory cells into 32 four-bit words.
c

## Slide 17: General Memory Operation
Diagram of a 32 x 4 memory, and the virtual arrangement of memory cells into 32 four-bit words.
Because this memory stores 32 words, it has 32 different storage locations & 32 different binary addresses, from 00000 to 11111 (0 to 31 in decimal).
There are five address inputs—A0 to A4.

## Slide 18: General Memory Operation
Diagram of a 32 x 4 memory, and the virtual arrangement of memory cells into 32 four-bit words.
To access one a memory location for read or write, the five-bit address code is applied to the address inputs. In general, N address inputs are required for a memory with a capacity of 2N words.

## Slide 19: General Memory Operation
Diagram of a 32 x 4 memory, and the virtual arrangement of memory cells into 32 four-bit words.
The WE (write enable) input is activated to allow the memory to store data.
The overbar indicates that the write operation takes place when WE = 0.

## Slide 20: General Memory Operation
Diagram of a 32 x 4 memory, and the virtual arrangement of memory cells into 32 four-bit words.
The OE pin is activated to enable the tristate buffer and deactivated to place the buffers in the high impedance (hi-Z) state.
A control signal connected to OE is active only when the bus is ready to receive data from the memory.

## Slide 21: CPU Memory Connections
Main memory is interfaced to the CPU through:
  Address bus; Data bus; Control bus.
The three buses play a necessary part in allowing the CPU to write data into memory and to read data from memory.

## Slide 22: CPU Memory Connections
Write operation process:
  The CPU supplies the binary address of the memory location where the data are to be stored.
    It places this address on the address bus lines.
  An address decoder activates the memory device’s enable input (CE or CS).
  CPU places data to be stored on the data bus lines.
  CPU activates appropriate control signal lines for the memory write operation
WR or R/W.
  Memory ICs internally decode the binary address to determine the location selected for the store operation.
  The data on the data bus are transferred to the selected memory location.

## Slide 23: CPU Memory Connections
Read operation process:
  The CPU supplies the binary address of the memory location from which data are to be retrieved.
    It places this address on the address bus lines.
  An address decoder activates the memory device’s enable input (CE or CS).
  The CPU activates the appropriate control signal lines for the memory read operation, which is normally connected to on the memory IC.
WR or R/W.
    Example:
  Memory ICs internally decode the binary address to determine the location is being selected to read.
    They place data from the memory location onto the data bus, from which they are transferred to the CPU.

## Slide 24: CPU Memory Connections
Function of each of the system buses:
  Address Bus—unidirectional bus that carries binary address outputs from the CPU to the memory ICs.
    To select one memory location.
  Data Bus—bidirectional bus that carries data between the CPU and the memory ICs.
  Control Bus—carries control signals ( ) from the CPU to the memory ICs.
RD or WR

## Slide 25: Read Only memories(ROM)
Read-only memory is semiconductor memory designed to hold data that are permanent or will not change frequently.
Some ROMs cannot have their data changed once they have been programmed—others can be erased & reprogrammed as often as desired.
  The process of entering data is called programming or burning the ROM.
A major use of ROMs storage of programs in microcomputers.
  As ROMs are nonvolatile, programs are not lost when electrical power is turned off.

## Slide 26: Read Only memories
Typical ROM

## Slide 27: Read Only memories
To read a data word from ROM requires:
  Applying the appropriate address inputs.
  Activating the control inputs.

## Slide 28: ROM Architecture
The internal architecture (structure) of a ROM IC is complex—but has four basic parts:
  Register array—stores data programmed into ROM.
    Each register contains several memory cells equal to the word size.
  Address decoders—Row & Column decoders.
    Only one register will be in both row & column selected by the address inputs, and this one will be enabled.
  Output buffers—pass data to external data outputs.
    The register that is enabled by the address inputs will place its data on the data bus.
    These data feed into the output buffers, which will pass the data to the external data outputs.

## Slide 29: ROM Architecture
Architecture of a 16 x 8 ROM. Each register stores one eight-bit word.

## Slide 30: ROM Timing
There will be propagation delay between the application of a ROM’s inputs and appearance of the data outputs during a read operation.
Called access time (tACC), the delay is a measure of ROM operating speed.

## Slide 31: ROM Timing
There will be propagation delay between the application of a ROM’s inputs and appearance of the data outputs during a read operation.
Another important timing parameter is output enable time (tOE ), the delay between input and valid data output.
Values for tOE are always shorter than access time.

## Slide 32: Types of ROMs
Mask-programmed ROM (MROM) has data stored at the time the IC is manufactured.
ROMs are made up of a rectangular array of transistors.
Information is stored by either connecting or disconnecting the source of a transistor to the output column.

## Slide 33: Types of ROMs
Mask-programmed ROM (MROM) has data stored at the time the IC is manufactured.
The last step in the manufacturing is to form all these conducting paths or connections.
The process uses a “mask” to deposit metals on the silicon that determine where connections form.

## Slide 34: Types of ROMs
The mask is very precise, expensive and must be made specifically for the customer, with the correct binary information.
  Economical only when many ROMs are being made with exactly the same information.

## Slide 35: Types of ROMs
For lower-volume applications, user-programmable fusible-link PROMs are available.
  Custom-programmed by the user, it cannot be erased and reprogrammed.
If information in the PROM is faulty or must be changed, it must be discarded.
Often referred to as “one-time programmable” (OTP) ROMs.

## Slide 36: Types of ROMs
An EPROM can be user-programmed, erased and reprogrammed as often as desired.
  Once programmed, it is a nonvolatile memory that will hold its stored data indefinitely.
A UV light is used to clear the device.

## Slide 37: Electrically Programmable ROM (EPROM)
The first EPROMs are based on floating-gate transistors depicted in figure

## Slide 38: Continue
A floating gate avalanche injection MOS transistor is different to conventional MOSFETS in that presents an additional gate known as a floating gate. This gate (with no connections) is surrounded by insulating material (SiO2) and has no connections to external circuitic. The regular gate is referred to as control gate.
If a large voltage is applied to the control gate (12V) and also to the drain (6V), with source grounded, high-energy electrons start flowing between the source and the drain terminals. Some of these electronics might acquire enough kinetic energy to traverse the thin (100nm) oxide layer that separates the transistor channel from the floating gate.
Once they reach the floating gate will be trapped and remain there indefinitely (if no opposing electric field is applied).
The presence of electronics in the floating gate raises the threshold voltage (VT) from 1V to over 6V.
Therefore, given that all logic are < or = 5V, such a transistor can never be turned on.
Thus a transistor without charge stored in the floating gate is said to be erased (this is considered a 1) while a transistor with a charge in the floating gate is said to be programmed (considered to 0).
The floating gate transistor is used to implement an EPROM array as shown in the figure.

## Slide 39
The main limitation of of EPROMs is the erase procedure. We have to us UV radiation to generate electron hole pairs in the insulator causing it to be slightly conductive for several minutes a process which is time consuming.
Another limitation is the erase endurance (only 100 times).

## Slide 40: Electrical Erasable Programmable ROM (EEPROM)
EEPROM solves the erase problem of EPROM with a slight modification in the floating gate transistor.
The new device is floating-gate tunneling-oxide transitor depicted in figure

## Slide 41: Types of ROMs
Major disadvantages of UVEPROMs:
  They must be removed from the circuit to be programmed and erased.
  The erase operation erases the entire chip.
  The erase operation takes up to 20 minutes.

## Slide 42: Types of ROMs
The major characteristic of electrically erasable PROM (EEPROM) is electrical erasability.
  Also the ability to erase and rewrite individual bytes in the memory array.
Because the internal process of storing a data value in an EEPROM is quite slow, the speed of the data transfer operation can also be slower.
  EEPROM devices are available in eight-pin packages interfaced to a two- or three-wire serial bus.

## Slide 43: Flash ROM
A flash memory is a combination of EPROM and EEPROM. It requires only one transistor per cell (like EPROM) which can be electrically erased and programmed (like EEPROM).
Its high density and low cost has made it the preferred choice when reprogrammable nonvolatile storage is needed.

## Slide 44: Continue
The original transistor for flash memories is ETOX (EPROM tunnel oxide) transistor introduced by intel in 1984.
The ETOX versions are depicted in the figure below

## Slide 46
ETOX cell operate on avalanche-injection for programming (EPROM) and tunneling for erase (EEPROM).
To avoid extra (cell access) transistor of EEPROM, in-bulk erase is done, which consists of erasing the whole chip.

## Slide 47: Flash Memory
A flash memory cell is like the simple single-transistor EPROM cell, with a cost considerably less than for EEPROM.

## Slide 48: Flash Memory
The unique feature of the 28F256A CMOS flash memory IC is the command register.
  Command codes are written into this register to control which operations take place inside the chip.
  State control logic examines the contents of the command register and generates logic and control signals.

## Slide 49: Flash Memory
The first flash devices, created to improve on EEPROM, used NOR flash technology.
  Circuit functions logically like a NOR gate.
    Each transistor can be read or written independent of the status of the other transistors in the group.

## Slide 50: Flash Memory
NOR flash offers quick read access time and random access.
  Usually used for things like storing program instructions for the microcontroller in your cell phone.

## Slide 51: Flash Memory
Attempts were made to improve density of mass-storage flash devices, resulting in the NAND flash.
  Data must be accessed in conjunction with the other word lines being activated by a control gate voltage.
  Activated by a control gate voltage large enough to turn on the other transistors—regardless of the amount of charge on the floating gate.

## Slide 52: ROM Applications
Here are some of the most common application areas in which ROMs are used:
  Embedded microcontroller program memory.
    Automotive automatic braking systems, cell phones, microwave ovens, etc.
  Data transfer and portability.
    Cell phones, digital cameras, flash drives, MP-3 players.
  Bootstrap memory.
    A relatively small program, stored in ROM loads the operating system programs from mass storage (disk) into a computer’s main internal memory.

## Slide 53: ROM Applications
Here are some of the most common application areas in which ROMs are used:
  Data tables.
    Tables of data that do not change like trigonometric and code-conversion tables.
  Data converter.
    Data expressed in one type of code is converted to an output expressed in another type, such as BCD to 7-segment LED readouts.

## Slide 54: ROM Applications
Here are some of the most common application areas in which ROMs are used:
  Function generator.
    Produces waveforms such as sine waves, sawtooth waves, triangle waves, and square waves.
A ROM look-up table and a DAC are used to generate a sine-wave output signal.

## Slide 55: Semiconductor RAM
RAM—random-access memory—means any memory address location is as easily accessible as any other.
Used in computers for temporary storage of programs and data—requires fast read/write cycle times to avoid slowing computer operation.
  RAM can be written into and read from rapidly with equal ease.
RAM is volatile and will lose all stored information if power is interrupted or turned off.
  Some CMOS RAMs can be powered from batteries when main power is interrupted.

## Slide 56: 12-11 RAM Architecture
It is helpful to think of RAM as consisting of a number of registers.
  Each storing a single data word, and each having a unique address.
Most memory chips have one or more CHIP SELECT (CS) inputs, used to enable the entire chip or disable it completely.
  In disabled mode, all data inputs outputs are disabled (Hi-Z)—neither a read nor a write can take place.
In order to conserve pins on an IC package, manufacturers often combine data input and output functions using common input/output pins.

## Slide 57: RAM Architecture
To READ the contents of the selected register:
The write enable input must be a 1.
WE or R/W
The CHIP SELECT input must also be activated.
Input buffers are disabled during a data read.

## Slide 58: RAM Architecture
To WRITE a four-bit word to the selected register:
The write enable input must be a 0.
WE or R/W
The CHIP SELECT input must also be a 0.
Tristate output buffers are in Hi-Z state during a data write.

## Slide 59: Static RAM (SRAM)
Static-RAM memory cells are essentially flip-flops that stay in a given state (store a bit) indefinitely.
  Provided power to the circuit is not interrupted.
Available in bipolar, MOS and BiCMOS variations
  The majority of applications today use CMOS RAMs.

## Slide 60: Static RAM (SRAM)
Timing diagram for a complete READ cycle for a typical RAM chip.

## Slide 61: 12-12 Static RAM (SRAM)
Timing diagram for a complete WRITE cycle for a typical RAM chip.

## Slide 62: 12-12 Static RAM (SRAM)
An example of an actual SRAM IC is the MCM6264C CMOS 8K x 8 RAM,
  Read- and write-cycle times of 12 ns.
  Standby power consumption of only 100 mW.

## Slide 63: 12-12 Static RAM (SRAM)
Industry standards created by the Joint Electronic Device Engineering Council (JEDEC) have led to memory devices that are interchangeable.

## Slide 64: 12-13 Dynamic RAM (DRAM)
Dynamic RAM stores data as charges on capacitors, which gradually disappear due to capacitor discharge.
  It is necessary to refresh the data periodically by recharging capacitors—typically every 2, 4, or 8 ms.
Much larger capacities and much lower power consumption make DRAMs the memory of choice.
  Where the most important design considerations are keeping down size, cost, and power.

## Slide 65: Dynamic RAM Structure and Operation
The dynamic RAM’s internal architecture can be visualized as an array of single-bit cells.
Cell arrangement in a 16K x 1 dynamic RAM.
Total = 16,384 cells.

## Slide 66: Dynamic RAM Structure and Operation
Essential ideas involved in writing to, and reading from a DRAM.
During a WRITE operation, switches SW1 and SW2 are closed. During a read operation, all switches are closed except SW1.

## Slide 67: 12-16 DRAM Refreshing
When a read operation is performed on a cell, all of the cells in the row will be refreshed.
Refresh control logic is used to make sure each row is refreshed within the time limit.
  In burst refresh mode, normal memory operation is suspended, and each row is refreshed in succession until all rows have been refreshed.
  In a distributed refresh, row refreshing is interspersed with the normal operations of the memory.

## Slide 68: 12-16 DRAM Refreshing
  It is performed by strobing in a row address with RAS while CAS and WE remain HIGH.
The most universal method for refreshing a DRAM is the RAS-only refresh.
A dynamic RAM (DRAM) controller is often used to perform address multiplexing and refresh count sequence generation.

## Slide 69: 12-17 DRAM Technology
Standard memory interface connectors are used.
  The connectors receive a small printed circuit card with contact points on both sides of the card edge.
    Allow easy memory component installation/replacement.
Memory modules:
  SIMM—single in-line memory module—a circuit card with 72 functionally equivalent contacts on both sides.
  DIMM—dual-in-line memory module (DIMM) has from 168 to 240 functionally unique pins on each side.
  SODIMM—small-outline, dual-in-line memory module for compact applications, such as laptop computers.
  RIMM—Rambus In-line Memory Module, a proprietary package that holds Direct Rambus DRAM (DRDRAM).

## Slide 70: 12-17 DRAM Technology
FPM DRAM—fast page mode (FPM) allows quicker access to random memory locations within the current “page.”
  A page is a range of memory addresses that have identical upper address bit values.
    Only the lower address lines must be changed.

## Slide 71: 12-17 DRAM Technology
EDO DRAM—Extended data output (EDO) DRAM offers a minor improvement to FPM.
  For accesses on a given page, the data value at the current memory location is sensed and latched onto the output pins.
  While these data are present on the outputs, a new address on the current page can be decoded, and data path circuitry can be reset for the next access.
    This allows the memory controller to be outputting the next address at the same time the current word is being read.

## Slide 72: 12-17 DRAM Technology
SDRAM—synchronous DRAM is designed to transfer data in rapid-fire bursts of several sequential memory locations.
  The first location accessed is the slowest due to the overhead (latency) of latching row & column address.
    After this data values are clocked by the bus system.
SDRAMs are organized in two (or more) banks.
  Allows data to be read out at a very fast rate by alternately accessing each of the two banks.
Self-refresh mode allows the memory device to perform all of the necessary functions to keep its cells refreshed.

## Slide 73: 12-17 DRAM Technology
DDRSDRAM—Double Data Rate SDRAM refers to the memory module’s interface to the PC bus.
  Achieves higher data rates by transferring data on the rising and falling edge of the system clock.
    Burst transfer rates twice as fast as the SDRAM ICs.
DDR2 uses buffering techniques to produce I/O data rates four times faster than the SDRAMs.
  DDR3 transfers data eight times faster.
Speeding up the system clock offers marginal improvement in performance—given that the SDRAM latency is the ultimate limiting factor of maximum speed.

## Slide 74: 12-18 Other Memory Techniques - Magnetic
The first method of magnetic storage of digital information involved reels of magnetic tape for long-term storage/retrieval of programs and data.

## Slide 75: END