## Slide 1: EEE3131 Digital Electronics
Lecture 2 : Number Systems & Codes
Instructor: George ZIBA
March 2021
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Email: George.ziba@unza.zm

## Slide 2: References
Our main reference text books in this course are
[1] William Kleitz, 2006, Digital Electronics with VHDL, Prentice Hall ISBN-100131714902 [Practical 1]
[2] Maini Anil K., Digital Electronics: Principles, Devices and Applications, 2007, John Wiley and Sons Ltd, ISBN 978-0-470-03214-5. [Theory 1]
[3] Thomas L. Floyd, 2006, Digital Fundamentals with PLD Programming, Prentice Hall ISBN-10: 0131701886 [Practical 2]
[4] Sedha R.S, A textbook of Digital Electronics, S. Chand, 2010 [Theory 2]
[5] Alan C. Diixon, JamesL. Antonakos, 2000, A Practical Approach To Digital Electronics, Prentice Hall ISBN-10: 0137275 951. [General Reference]
**NOTE: theory 1 and practical 1 have high preference for practical and theory respectively
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 3: Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Introductory Digital Concepts:
Digital and Analog Quantities. Binary Digits, Logic Levels, and Digital Waveforms. Introduction to Logic Operations. Basic Overview of Logic Functions. Fixed-Function Integrated Circuits. Circuit Design Using Programmable Logic Basics: VHDL/Verolog.
Number Systems, Operations, and Code:
Decimal Numbers. Binary Numbers. Decimal-to-Binary Conversion. Binary Arithmetic. 1s and 2s Complements of Binary Numbers. Signed Numbers. Arithmetic Operations with Signed Numbers. Hexadecimal Numbers. Octal Numbers. Binary Coded Decimal (BCD). Digital Codes and Parity. Numeric Values in VHDL.
Logic Fundamentals:
Logic Gates. Fixed-Function Logic: IC Gates. Laws and Rules of Boolean Algebra.. Boolean Analysis of Logic Circuits. Simplification Using Boolean Algebra. Boolean Expressions and Truth Tables. The Karnaugh Map. Karnaugh Map SOP Minimization. Karnaugh Map POS Minimization. Boolean Expressions with VHDL. Digital System Application.

## Slide 4
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
4
Combinational Logic Circuits and Logic functions:
Basic Combinational Logic Circuits. Implementing Combinational Logic. The Universal Property of NAND and NOR Gates. Combinational Logic Using NAND and NOR Gates. Logic Operation with Pulse Waveform Inputs . Binary adders/ subtractors. Comparators. Encoders/Multiplexers. Decoders/Demultiplexers. Code Converters, A/D and D/A Converters. Parity Generators/Checkers. Design examples using HDL.
Synchronous Sequential/ Asynchronous Logic Circuits:
S-R latch, clocked S-R flip flop, level and edge triggering. Master-slave, propagation delay, ac coupled, and capacitive storage 'edge' triggering techniques in flip flops. J-K, T, and D type flip flops. Timers and Counters. Serial/Parallel in/out Shift Registers. Truth tables and Excitations Tables; State Diagrams and State Transitions Tables; State Machines; State Reduction, Races, Hazards. Shift Registers Using VHDL. Digital System Application.

## Slide 5
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
5
Memory and Storage :
Basics of Semiconductor Memory. Random-Access Memories (RAMs). Read-Only Memories (ROMs). Programmable ROMs (PROMs and EPROMs); PLAs . Flash Memories. Memory Expansion. Magnetic and Optical Storage. Design examples using HDL.
Integrated Circuit Technologies :
Basic Operational Characteristics and Parameters. CMOS Circuits. TTL Circuits. Practical Considerations in the Use of TTL. Comparison of CMOS and TTL Performance. Emitter-Coupled Logic (ECL) Circuits. Application-Specific integrated Circuits (ASICs), PMOS, NMOS, and E2CMOS.
Introduction to Microprocessors, Computers, and Buses :
The Microprocessor and the Computer. Historical Review of Microprocessor Families. The 8086/8088 Microprocessor and Software Model for the Pentium Processor. Microprocessor Programming. The Central Processing Unit (CPU). The Memory. The Input/Output (I/O) Port. Interrupts. Direct Memory Access (DMA). Internal System Interfacing. Standard Buses.

## Slide 6: Course Requirements
Prerequisite
EEE 3571 Electronic Engineering I (Analog Electronics)
Distribution of Marks
Assignments 5%
Labs 15%
Test 20%
Final Exam 60%
Required Simulation software and Programming Language
Multisim
Intel Quartus Prime
C++
Time Allocation
Lectures 4 hours/week
Laboratory/ Tutorials 3 hours/week
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 7: Introduction
To process digital information we use special electronic components that respond to binary signals.
To design efficient digital circuits, we also need a special numbering system and a special algebra.
In this course, first we examine the binary number system and learn to apply logic theorems to binary relations.
Computers consist of large numbers of logic gates and memory elements organized to process data at high speed.
Binary data or instructions are stored temporarily in registers. Binary counters are used in calculations and to keep track of computer operations.
Instructions and data are stored at specified locations in memory and can be retrieved at will.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 8: Introduction
Objectives of Lectures
On completion of the Lectures on Number systems and codes, you should be able to work in the binary number system as well as the decimal system. In addition, you should be able to change a number from one base to another.
On completion of the Lectures on Logic fundamentals, you should be able to use basic theorems to simplify and analyse logic functions in common use. Furthermore, you should be able to simplify logic expressions using Karnaugh maps.
This therefore, will set a foundation for the material you will study later on combinational logic ckts, sequential logic ckts and finally microprocessors.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 9: Binary Numbers
In the decimal number system a quantity is represented by the value and the position of a digit. The number 503.14 means
Using powers of 10, this can be rewritten as
In other words, 10 is the base and each position to the left or right of the decimal point corresponds to a power of 10.
A base 12 or duodecimal system was used by the Babylonians, and we still use 12 in subdividing the foot, the year, and the clock face.
In representing data by an ON-OFF switch position, there are two possibilities and the corresponding numbers are 1 and 0.
In such a binary system, the base is 2 and the decimal number 10 is written as 1010 since
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 10: Binary Numbers
In electronic logic circuits the numbers 1 and 0 usually correspond to two easily distinguished voltage levels specified by the circuit designer. For instance, in TTL (Transistor Transistor Logic), 0 corresponds to a voltage near zero and 1 to a voltage near +5 V.
Number Conversion
Binary-to-decimal conversion. In a binary number, each position to the right or left of the “binary point” corresponds to a power of 2, and each power of 2 has a decimal equivalent.
To convert a binary number to its decimal equivalent, add the decimal equivalents of each position occupied by a 1.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 11: Binary Numbers
For instance,
Decimal-to-binary conversion. A decimal number can be converted to its binary equivalent by the inverse process, that is, by expressing the decimal number as a sum of powers of 2.
An automatic and more popular method is the double-dabble in which integers and decimals are handled separately.
To convert a decimal integer to its equivalent, progressively divide the decimal number by 2, noting the remainders; the remainders taken in reverse order form the binary equivalent.
To convert a decimal fraction to its binary equivalent, progressively multiply the fraction by 2, removing and noting the carries; the carries taken in forward order form the binary equivalent.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 12: Binary Numbers
Example 1
Convert decimal 28.375 to its binary equivalent.
Solution. Using the double-dabble method on the integer,
The binary equivalent is 11100.
Then converting the fraction
The binary equivalent is .011.
Therefore, 28.375 is equivalent to binary 11100.011.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 13: Binary Numbers
Binary Arithmetic
Since the binary system uses the same concept of value and position of the digits as the decimal system, we expected the associated arithmetic to be similar but easier.
The binary multiplication table is very short. For addition in binary, we add column by column, carrying where necessary into higher position columns.
In subtraction, we subtract column by column, borrowing where necessary from higher position columns.
In subtracting a large number from a smaller, we can subtract the smaller from the larger and change the sign just as we do with decimals.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 14: Binary Numbers
Example 2
Convert the numbers in color to the other form and perform the indicated operations.
In multiplication, we obtain partial products using the binary multiplication table, and then add the partial products.
In division, we perform repeated subtractions just as in long division of decimals, See Example 3.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 15: Binary Numbers
Example 3
Convert the numbers in color to the other form and perform the indicated operations.
(a)
(b)
(a)
(b)
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 16: Binary Numbers
Bits, Bytes, and Words
A single binary digit is called a “bit.” All information in digital system is represented by a sequence of bits. An 8-bit sequence is called a “byte”; a 4-bit sequence is a “nibble.”
The number of bits in the data sequences processed by a given computer is a key characteristic called the “word length”. Computers handle data in words of 4 to 64 bits.
An 8-bit microprocessor can receive, process, store, and transmit data or instructions in form of bytes. Eight bits can be arranged in different combinations.
Other Notations
The number of years in a century can be written 100D or . In binary notation this would be written or
; the prefix B or subscript 2 is used whenever necessary to avoid confusion.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 17: Binary Numbers
Other Notations
Although 8-bit numbers are easy for computers, they are difficult for humans to deal with. In octal notation, a single decimal number from 0 to 7 is used to represent each group of three bits.
As an octal number, would be written as
. Three-digit octal numbers are easier to remember and easier to check than their 8-bit binary equivalents.
In the alternative notation most commonly used in microprocessor work, each group of four bits is represented by single hexadecimal number.
In “hex,” would be written as . Because four bits can take on sixteen different values, we supplement the ten decimal digits 0 to 9 with letters A, B, C, D, E and F.
For example, and
. Table 1 shows the various notations discussed thus far.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 18: Binary Numbers
Signed Magnitudes
In binary notation, an n-bit data word can represent the first nonnegative integers.
Table 1 Number Systems
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 19: Binary Numbers
Signed Magnitudes
To allow for both positive and negative numbers, the most significant bit (MSB) can be designated as the sign bit (1 for negative numbers).
The lower order bits then represent the magnitude of the number in “straight” binary notation.
Although it is used, this arrangement has two disadvantages: the number zero has two different representations, and two different arithmetic circuits are required to process positive and negative numbers.
Two’s Complement Notation
A better notation for computers, one that is easily implemented in hardware, is based on the fact that adding the complement of a number is equivalent to subtracting the number.
A “complement” is that which completes; the “n’s complement” of a number x is equal to .
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 20: Binary Numbers
Two’s Complement Notation
For example, the 10’s complement of 3 is 7. To evaluate , i.e., to subtract 3 from 9, we can “add the 10’s complement” of 3 (i.e., ) to obtain
to yield 6 after discarding the final carry.
In the decimal system, the 10’s complement of a multidigit number is easily found by taking the 9’s complement of each digit (by inspection) and then adding 1.
In general, to subtract a two-digit number B from A we use the relationship
[1]
where is the 9’s complement.
In the binary system, arithmetic is simplified if negative numbers are in signed 2’s complement notation. In this notation, the MSB is the sign bit: 0 for plus, 1 for minus. To form the 2’s complement of any number, positive or negative:
Form the 1’s complement by changing 1s to 0s and 0s to 1s. Add 1.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 21: Binary Numbers
Example 4
Obtain the 10’s complement of 15 and 24.
Represent and in 8-bit signed 2’s complement notation.
Perform and directly and by complement notation.
Solution
Form the 9’s complement of each digit, then add 1:
Form the 1’s complement of each digit, then add 1.
If the result of an arithmetic operation has a 1 sign bit, it is a negative number in 2’s complement notation; to obtain the true magnitude, subtract 1 and form the 1’s complement.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 22: Binary Numbers
Example 4
c) Solution
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 23: Binary Numbers
Binary-Coded Decimals (BCD)
For the convenience of humans, computer input/output devices may accept/provide decimals on the human side and binaries on the computer side.
The conversion is simplified by coding each decimal digit, that is, replacing it by the 4-bit binary representation of the digit.
For example, in the 8421 BCD code , , and
.
BCD-to-Binary Conversion. A given BCD number can be converted into an equivalent binary number by first writing it decimal equivalent and then converting it into its binary equivalent.
Binary-to-BCD Conversion. The process is the same as the process of BCD-to-binary conversion executed in reverse order.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 24
Excess-3 Code
It is particularly significant for arithmetic operations as it overcomes the shortcomings encountered while using the 8421 BCD code to add two decimal digits whose sum exceeds 9.
The excess-3 code for a given decimal number is determined by adding ‘3’ to each decimal digit in the given number and then replacing each digit of the newly found decimal number by its four bits binary equivalent.
Binary Numbers
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
22

## Slide 25: Binary Numbers
Gray Code
The Gray code was designed by Frank Gray at Bell Labs and patented in 1953. It is an unweighted binary code in which two successive values differ only by 1 bit.
Owing to this feature, the maximum error that can creep into a system using Gray code to encode data is much less than the worst-case error encountered in the case of straight binary encoding. Table 2 list Gray code equivalents of decimal numbers 0 – 15.
Table 2 Gray code.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 26: Binary Numbers
Gray Code
There are various ways by which Gray codes with a given number of bits can be remembered. One such a way is to remember that the least significant bit follows a repetitive pattern of ‘2’ (11, 00, 11, …), the next higher adjacent bit follows a pattern of ‘4’ (1111, 0000, 1111, …) and so forth.
Binary to Gray Code Conversion steps
Step 1. Begin with the most significant bit (MSB). The MSB of the Gray code equivalent is the same as the MSB of the given binary number.
Step 2. The second MSB in the Gray code number is obtained by adding the MSB and the second MSB in the binary number and ignoring the carry, if any.
Step 3. The third MSB in the Gray code number is obtained by adding the second MSB and the third MSB in the binary number, ignore carry.
Step 4. The process continues until we obtain the LSB of Gray code number.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 27: Binary Numbers
Example 5
Convert the Binary number 1011 into its Gray code equivalent.
Solution
Binary 1011
Gray code 1- - -
Binary 1011
Gray code 11
Binary 1011
Gray code 111
Binary 1011
Gray code 1110
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 28: Binary Numbers
Gray Code
Gray Code to Binary Conversion steps
Step 1. Begin with the most significant bit (MSB). The MSB of the binary number is the same as the MSB of the Gray code number.
Step 2. The bit next to the MSB (second MSB) in the binary number is obtained by adding the MSB in the binary number to the second MSB in the Gray code number and disregarding the carry, if any.
Step 3. The third MSB in the binary number is obtained by adding the second MSB in the binary number to the third MSB in the Gray code number. Ignored carry.
Step 4. The process continues until we obtain the LSB of binary number.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 29: Binary Numbers
Example 6
Convert the Gray code number 1110 into its binary equivalent.
Solution
Gray code 1110
Binary 1- - -
Gray code 1110
Binary 10- -
Gray code 1110
Binary 101
Gray code 1110
Binary 1011
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 30: Binary Numbers
Applications of Gray codes
The Gray code is used in the transmission of digital signals as it minimizes the occurrence of errors.
The Gray code is preferred over the straight binary code in angle-measuring devices.
The Gray code is used for labeling Karnaugh maps, a graphical technique used for minimizing of Boolean expressions.
The use of Gray codes to address program memory in computers minimizes power consumption. This is due to fewer address lines changing state with advances in the program counter.
Gray codes are also useful in genetic algorithms.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 31: Binary Numbers
Alphanumeric Codes
When a computer is to handle letters as well as numbers, an alphanumeric code is used. In the American Standard Code for Information Interchange (ASCII), seven bits are used to represent all the characters and punctuation marks on a teletypewriter keyboard plus some control signals.
Note that, combinations of 7 bits. An eighth bit, the MSB, is a parity bit used in error detection. In even parity convention, the MSB is set so that the 1s in each ASCII character is even; the presence of an odd number of 1s indicates an error.
In reference [2], the ASCII code is listed in a table starting from page 40.
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 32
Tutorial
Convert the decimal fraction 0.9028 to its equivalent binary fraction (up to 4 binary places) using repeated multiplication-by-2 method. 0.9028 = 0.1110 Ans.
Convert the decimal 0.8125 to its binary equivalent.(Gujarat Technological University, Dec 2009). 0.8125 = 0.11010. Ans.
Obtain the binary equivalent of 15 and 25. (Gauhati University, 2007). 15= 1111 Ans. 25 = 11001 Ans.
Convert each of the following decimal numbers to their binary equivalents using sum-of-weights methods: (a) 17 (b) 24 (c) 61 (d) 93.
(a) 17= 10001 Ans. (b) 24 = 11000 Ans. (c) 61 = 111101 Ans. (d) 93 = 1011101 Ans.

## Slide 33: End of Lecture 2
Thank you for your attention!
George ZIBA , DEPT. of EEE, School of Engineering, UNZA