## Slide 1: EEE3131 Digital Electronics
Lecture 1 : Analogue vs Digital Systems
Instructor: George ZIBA
March 2021
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Email: george.ziba@unza.zm
0976854627

## Slide 2: References
Our main reference text books in this course are
[1] William Kleitz, 2006, Digital Electronics with VHDL, Prentice Hall ISBN-100131714902 [Practical 1]
[2] Maini Anil K., Digital Electronics: Principles, Devices and Applications, 2007, John Wiley and Sons Ltd, ISBN 978-0-470-03214-5. [Theory 1]
[3] Thomas L. Floyd, 2006, Digital Fundamentals with PLD Programming, Prentice Hall ISBN-10: 0131701886 [Practical 2]
[4] Sedha R.S, A textbook of Digital Electronics, S. Chand, 2010 [Theory 2]
[5] Alan C. Diixon, JamesL. Antonakos, 2000, A Practical Approach To Digital Electronics, Prentice Hall ISBN-10: 0137275 951. [General Reference]
**NOTE: theory 1 and practical 1 have high preference for practical and theory respectively
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 3: Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
Introductory Digital Concepts:
Digital and Analog Quantities. Binary Digits, Logic Levels, and Digital Waveforms. Introduction to Logic Operations. Basic Overview of Logic Functions. Fixed-Function Integrated Circuits. Circuit Design Using Programmable Logic Basics: VHDL/Verolog.
Number Systems, Operations, and Code:
Decimal Numbers. Binary Numbers. Decimal-to-Binary Conversion. Binary Arithmetic. 1s and 2s Complements of Binary Numbers. Signed Numbers. Arithmetic Operations with Signed Numbers. Hexadecimal Numbers. Octal Numbers. Binary Coded Decimal (BCD). Digital Codes and Parity. Numeric Values in VHDL.
Logic Fundamentals:
Logic Gates. Fixed-Function Logic: IC Gates. Laws and Rules of Boolean Algebra.. Boolean Analysis of Logic Circuits. Simplification Using Boolean Algebra. Boolean Expressions and Truth Tables. The Karnaugh Map. Karnaugh Map SOP Minimization. Karnaugh Map POS Minimization. Boolean Expressions with VHDL. Digital System Application.

## Slide 4
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
4
Combinational Logic Circuits and Logic functions:
Basic Combinational Logic Circuits. Implementing Combinational Logic. The Universal Property of NAND and NOR Gates. Combinational Logic Using NAND and NOR Gates. Logic Operation with Pulse Waveform Inputs . Binary adders/ subtractors. Comparators. Encoders/Multiplexers. Decoders/Demultiplexers. Code Converters, A/D and D/A Converters. Parity Generators/Checkers. Design examples using HDL.
Synchronous Sequential/ Asynchronous Logic Circuits:
S-R latch, clocked S-R flip flop, level and edge triggering. Master-slave, propagation delay, ac coupled, and capacitive storage 'edge' triggering techniques in flip flops. J-K, T, and D type flip flops. Timers and Counters. Serial/Parallel in/out Shift Registers. Truth tables and Excitations Tables; State Diagrams and State Transitions Tables; State Machines; State Reduction, Races, Hazards. Shift Registers Using VHDL. Digital System Application.

## Slide 5
Course Outline
George ZIBA , DEPT. of EEE, School of Engineering, UNZA
5
Memory and Storage :
Basics of Semiconductor Memory. Random-Access Memories (RAMs). Read-Only Memories (ROMs). Programmable ROMs (PROMs and EPROMs); PLAs . Flash Memories. Memory Expansion. Magnetic and Optical Storage. Design examples using HDL.
Integrated Circuit Technologies :
Basic Operational Characteristics and Parameters. CMOS Circuits. TTL Circuits. Practical Considerations in the Use of TTL. Comparison of CMOS and TTL Performance. Emitter-Coupled Logic (ECL) Circuits. Application-Specific integrated Circuits (ASICs), PMOS, NMOS, and E2CMOS.
Introduction to Microprocessors, Computers, and Buses :
The Microprocessor and the Computer. Historical Review of Microprocessor Families. The 8086/8088 Microprocessor and Software Model for the Pentium Processor. Microprocessor Programming. The Central Processing Unit (CPU). The Memory. The Input/Output (I/O) Port. Interrupts. Direct Memory Access (DMA). Internal System Interfacing. Standard Buses.

## Slide 6: Course Requirements
Prerequisite
EEE 3571 Electronic Engineering I (Analog Electronics)
Distribution of Marks
Assignments 5%
Labs 15%
Test 20%
Final Exam 60%
Required Simulation software and Programming Language
Multisim
Intel Quartus Prime
C++
Time Allocation
Lectures 4 hours/week
Laboratory/ Tutorials 3 hours/week
George ZIBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 7
Outline
Introduction
Examples of Physical Quantities
Analogue way
  Merits and demerits of analogue systems
Digital way
  Merits and demerits of digital systems
Binary Digits
Logic Levels
Digital waveform
Tutorial
References

## Slide 8
Introduction
two basic ways of representing the numerical values of the various physical quantities:
  analogue
  Digital
choice of method depends on application and covinience

## Slide 9
Etc
Examples of Physical Quantities
Position
Velocity
Acceleration
Force
Pressure
Temperature
Flowrate
Voltage

## Slide 10
Analogue Way
express the numerical value of the quantity as a continuous range of values between the two expected extreme values.
For example, the temperature of an oven settable anywhere from 0 to 100 °C may Be measured to be 65 °C or 64.96 °C or 64.958 °C or even 64.9579 °C and so on, depending upon the accuracy of the measuring instrument

## Slide 11
Advantages of Analogue Systems
Self Study!!!!!

## Slide 12
Disadvantages of Analogue Systems
Difficulty to design
Low accuracy
Non-programmability
Susceptible to noise
Difficulty storage of data
Difficulty of fabrication in integrated circuit form, size challenges

## Slide 13
Digital way
represents the numerical value of the quantity in steps of discrete values.
The numerical values are mostly represented using binary numbers.
For example, the temperature of the oven may be represented in steps of 1 °C as 64 °C, 65 °C, 66 °C and so on.

## Slide 14
Advantages of digital systems
relatively much easier to design
higher accuracy
programmability
noise immunity
easier storage of data
ease of fabrication in integrated circuit form, leading to availability of more complex functions in a smaller size.

## Slide 15
Disadvantage of digital system
Thus most of the physical quantities in nature are analog.
Require analogue t digital conversion and vice versa
added complexity and expense.
an extra time is required to perform these conversions.
However, we must understand that, these factors are outweighed by the numerous advantages of using digital techniques.

## Slide 16
The Binary Digits
The binary number system (which you will study later ) makes use of two digits 1 and 0.
These two digits are called bits.
The term bit is a contraction of binary digit.

## Slide 17
The Binary Digits
In order to represent numbers, letters, symbols instructions and anything else required in a given application (to be implemented by a digital systems), we make use of groups of bits.
Such groups of bits are called codes.

## Slide 18
In digital circuits, two different voltage levels are used to represent the two bits.
A 1 is represented by the higher voltage, which is referred to as a HIGH.
A 0 is represented by the lower voltage and is referred to as a LOW.
This is called positive logic and will be used throughout this course. Thus,
HIGH = 1 and LOW = 0
A much less common system in which a 1 is represented by a LOW Voltage and a 0 is represented by a HIGH is called negative logic.
Logic Levels

## Slide 19
A digital waveforms consist of voltage levels that are changing back and forth between the HIGH and LOW states.
These can also be described as the one that is composed of series of pulses,or a pulse train as shown in Fig. 1.
Digital Waveforms

## Slide 20
Waveform terms
It may also be noted that a pulse has two edges:
  (1) a rising edge and
  (2) a falling edge.
The rising edge in a positive-going pulse is also known as leading edge and the falling edge as the trailing edge.

## Slide 21
Rising and falling edge
A rising edge is a one that occurs when a voltage (or a current) goes from its normally LOW level to its HIGH level.
A falling edge is a one that occurs when a voltage (or current) goes from its HIGH level back to LOW level.

## Slide 22
practical digital circuit pulse
Consider a pulse below:

## Slide 23
Rise and fall time
The time required for the pulse to go from its LOW voltage level to its HIGH voltage level is called the rise time (tr)
the time required for the transition from the HIGH voltage level to the LOW voltage level is called the fall time (tf ).
It may be noted that the bottom 10% and the top 10% of the pulse are not included in the rise and fall times because of the non-linearity in the waveform in these areas.

## Slide 24
The Pulse Width (tw ) is a measure of the duration of the pulse and
is often defined as the time interval between the 50% points on the rising and falling edges
Pulse width

## Slide 25
Overshoot and Ringing.
These are undesirable pulse characteristics.
The overshoot could be positive and negative.
The overshoot is caused by a capacitive effect in the circuit or measuring instrument that results in the voltage exceeding the normal HIGH and LOW levels for a short time.
Ringing, on the rising and falling edges of a pulse, is actually an oscillation caused by capacitance and inductance in the circuit.

## Slide 26
Overshoot and Ringing.
Consider the diagram below illustrating overshoot and ringing:

## Slide 27
Period and frequency
When a digital wave form repeats itself, it is periodic
the rate at which it repeats itself is called frequency.

## Slide 28
Period and frequency
The two are related as:
……………………………………(3)
………………………………………(4)

## Slide 29
Duty cycle
An important characteristic of a periodic digital waveform is its duty cycle.
The duty cycle is defined as the ratio of the pulse width (tw) to the period (T) expressed as a percentage:

## Slide 30
Tutorial
Question one
Describe the merit and shortcomings of a digital signal.
Differentiate between positive logic and negative logic.
Explain the following terms as applied in digital waveforms:
  Rising edge
  Falling edge
  Rise time
  Fall time
  Overshoot
  Ringing

## Slide 31
Tutorial
Question two
define the terms pulse width and duty cycle
Figure 1 shows a portion of a periodic digital waveform. The measurements are in milliseconds. Determine the following:
  period
  frequency
  Duty cycle

## Slide 32
End of Lecture 1
Thank you for your attention!