## Slide 1: EEE 3131 - Digital Electronics
Lecture 2 : Logic Fundamentals
Instructor: Jerry MUWAMBA
October 2015
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Email: jerry.muwamba@unza.zm
jerrymuwamba@yahoo.com

## Slide 2: References
Our main reference text books in this course are
[1] Smith R. J., Dorf R. C., Circuits Devices and Systems, 5th Ed., 2004, John Wiley and Sons Ltd, ISBN 9971-51-172-X.
[2] Maini Anil K., Digital Electronics: Principles, Devices and Applications, 2007, John Wiley and Sons Ltd, ISBN 978-0-470-03214-5.
However, feel free to use some additional text which you might find relevant to our course.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 3: Introduction
We have seen that binary arithmetic and decimal arithmetic are similar in many respects. To work with logic relations in digital form, we need a set of rules for symbolic manipulation that will enable us to simplify complex expressions and solve for unknowns.
Simply put, we need a digital algebra. Nearly 100 years before the first digital computer, George Boole, an English mathematician (1815-1864), formulated a basic set of rules governing the true-false statements of logic.
Eighty-five years later (1938), Claude Shannon , at that time a graduate student a MIT, pointed out the usefulness of Boolean algebra in solving telephone switching problems and established the analysis of such problems on a firm mathematical basis.
Boolean algebra is valuable in manipulating binary variables in OR, AND, or NOT relations and in the analysis and design of all types of digital systems.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 4: Introduction
Logic gates are electronic circuits that can be used to implement the most elementary logic expressions also known as Boolean expressions.
The logic gate is the most basic building block of combinational logic. There are three basic logic gates, namely the OR gate, the AND gate and the NOT gate.
Other logic gates that are derived from these basic gates are the NAND gate, the NOR gate, the EXCLUSIVE-OR gate and the EXCLUSIVE-NOR gate.
Truth Table
A truth table lists all possible combinations of input binary variables and the corresponding outputs of a logic system.
When the number of input binary variables is only one, then there are only two possible inputs, i.e., ‘0’ and ‘1’.
If the number of inputs is two, there can be four possible input combinations, i.e., 00, 01, 10 and 11.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 5: Logic Gates
OR Gate
An OR gate performs an ORing operation on two or more logic variables. The OR operation on two independent logic variables A and B is written as
and reads as Y equals A OR B.
An OR gate is a logic circuit with two or more inputs and one output. The output of an OR gate is LOW only when all of its inputs are LOW, otherwise, it is HIGH for all other possible input combinations.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 1: Two-input OR gate.
Figure 1 shows the logic circuit symbol and truth table of a two-input OR gate.

## Slide 6: Logic Gates
AND Gate
An AND gate is a logic ckt having two or more inputs and one output. Its output is HIGH only when all of its inputs are in the HIGH state.
In all other cases, the output is LOW. The logic symbol and truth table of a two input AND gate are shown in Figure 2.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 2: Two-input AND gate.
The AND operation on two independent logic variables A and B is written as
and reads as Y equals A AND B.

## Slide 7: Logic Gates
Not Gate
A NOT gate is a one-input, one-output logic ckt whose output is always the complement of the input. That is, a LOW input produces a HIGH output, and vice versa.
Figure 3 shows the circuit symbol and the truth table for a NOT gate.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 3: Circuit symbol and truth table of a NOT ckt.
The NOT operation on a logic variable X is denoted as or . That is, if X is the input to a NOT ckt, then its Y is given by and reads as Y equals NOT X.

## Slide 8: Logic Gates
Exclusive-OR Gate
Commonly written as EX-OR gate, is a two-input gate. Its output is logic ‘1’ when the inputs are unlike and logic ‘0’ when the inputs are like.
The output of a multiple-input EX-OR logic function is a logic ‘1’ when the number of 1s in the input sequence is odd and logic ‘0’ when the number of 1s in the input sequence is even, including zero.
That is an all 0s input sequence also produces a logic ‘0’ at the output.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 4: Circuit symbol and truth table of an EX-OR ckt.
The output of a two-input EX-OR gate is expressed by

## Slide 9: Logic Gates
NAND Gate
NAND stands for NOT AND. An AND gate followed by a NOT circuit makes it a NAND gate. NAND gate operation is logically expressed as .
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 5: Circuit symbol and truth table of a NAND gate.
Figure 5 shows the circuit symbol and the truth table of a two-input NAND gate.

## Slide 10: Logic Gates
NOR Gate
NOR stands for NOT OR. An OR gate followed by a NOT ckt makes it a NOR gate. The output of a two-input NOR gate is logically expressed as
.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 6: Circuit symbol and truth table of a NOR gate.
Figure 6 shows the circuit symbol and the truth table of a two-input NOR gate.

## Slide 11: Logic Gates
Exclusive-NOR Gate
EX-NOR means NOT of EX-OR, i.e., the logic gate that we get by complementing the output of an EX-OR gate. Logically the output is given by
.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 7: Circuit symbol and truth table of a EX-NOR gate.
Figure 7 shows the circuit symbol and the truth table of a two-input EX-NOR gate.
The output of a two-input EX-NOR gate is a logic ‘1’ when the inputs are like and logic ‘0’ when they are unlike.

## Slide 12: Boolean Algebra
Boolean algebra is mathematics of logic. It is one of the most basic tools available to the logic designer and thus can be effectively used for simplification of complex logic.
Boolean algebra, quite interestingly, is simpler than ordinary algebra. It is also composed of a set of symbols and a set of rules to manipulate these symbols. Nevertheless, the differences between Boolean and ordinary algebra are as follows:
In ordinary algebra, the letter symbols can take on any number of values including infinity. In Boolean algebra, they can take on either of two values, that is, 0 and 1.
The values assigned to a variable have a numerical significance in ordinary algebra, whereas in its Boolean counterpart they have a logical significance.
While ‘ ’ and ‘+’ are respectively the signs of multiplication and addition in ordinary algebra, in Boolean algebra ‘ ’ means AND operation and ‘+’ means an OR operation.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 13: Boolean Algebra
Boolean algebra captures the essential properties of both logic operations such as AND, OR and NOT and set operations such as intersection, union and complement.
Boolean algebra may also be defined to be a set A supplied with two operations of logical AND , logical OR , a unitary operation NOT
, and two elements, namely logical FALSE and logical TRUE . This set is such that, for all elements of this set, the postulates or axioms relating to the associative, commutative, distributive , absorption and complementation properties of these elements hold good.
Postulates of Boolean Algebra
.
.
.
.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 14: Boolean Algebra
Many theorems of Boolean algebra are based on these postulates, which can be used to simplify Boolean expressions.
Theorems of Boolean Algebra
Theorem 1 (Operations with ‘0’ and ‘1’)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
where X is not necessarily a single variable – it could be a term or even a large expression.
Proof of theorem 1(a): we substitute all possible values of X, that is, 0 and 1, into the give expression and check if the LHS equals the RHS.
For .
For .
Thus , irrespective of the value of X, and hence the proof.
Proof of theorem 1(b) is similar: In general, according to theorem 1,
.
[1]

## Slide 15: Boolean Algebra
For example, and , where A, B and C are Boolean variables.
Theorem 2 (operations with ‘0’ and ‘1’)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
where X could be a variable, a term or even a large expression.
Proof of theorem 2(a):.
For .
For .
Proof of theorem 2(b) is similar: In general, according to theorem 2,
and
.
For example,
[2]

## Slide 16: Boolean Algebra
Theorem 3 (Idempotent or Identity Laws)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Theorem 3(a) is a direct consequence of an AND gate operation, whereas theorem 3(b) represents an OR gate operation when all inputs of the gate have been tied together.
The scope of the idempotent laws can be expanded further by considering X to be a term or an expression.
Example 1
Apply idempotent laws to simplify the Boolean expression
Solution
[3]

## Slide 17: Boolean Algebra
Theorem 4 (Complementation Law)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
By this theorem, in general, any Boolean expression when ANDed to its complement yields a ‘0’ and when ORed to its complement yields a ‘1’, irrespective of the complexity of the expression.
Proof of theorem 4(a):
For .
For .
Hence, theorem 4(a) is proved. Since theorem 4(b) is the dual of theorem 4(a), its proof is implied.
To further illustrate the application of theorem 4, consider
[4]

## Slide 18: Boolean Algebra
Example 2
Simplify the following:
Solution
We know that .
Also, is the complement of and is the complement of .
Therefore, the given expression reduces to .
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Theorem 5 (Commutative Laws)
[5]
Theorem 5(a) implies that the order in which variables are add or ORed is immaterial. Theorem 5(b) implies that the order in which variables are ANDed is also immaterial.

## Slide 19: Boolean Algebra
Theorem 6 (Associative Laws)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
[6]
Theorems 6(a) and (b) are further illustrated by the logic diagrams in Figures 8 (a) and (b).,
Figure 8: Associative laws.

## Slide 20: Boolean Algebra
Theorem 7 (Distributive Laws)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
[7]
Theorem 7(b) is the dual of theorem 7(a).
The proof of theorem 7(a) is done by means of perfect induction method, see table 1. Theorem 7(b) is the dual of theorem 7(a) and therefore its proof is implied
Table 1 Proof of distributive law.

## Slide 21: Boolean Algebra
Example 3 Illustration of Distributive Laws
Simplify the expressions and
.
Solution. Using the theorem 7(a) and (b) we have
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Theorem 8
This is a special case of theorem 7. Theorem 8 can be usefully employed to simplify many complex Boolean expressions.
[8]

## Slide 22: Boolean Algebra
Example 4 Illustration of theorem 8.
Simplify the expressions
and
.
Solution.
In the above expression, variables B, C and D are present in all eight possible combinations, and the variable A is common in all eight product terms. By theorem 8(a), this expression reduces to A.
By theorem 8(b) the second expression reduces to A as the variables B and C are present in all four possible combinations in sum terms and variable A is the common factor in all the terms.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 23: Boolean Algebra
Theorem 9
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
The Proof of theorem 9(a) is quite trivial.
Theorem 9(b) is the dual of theorem 9(a) and hence stands proved.
Theorem 10 (Absorption Law or Redundancy Law)
The Proof of absorption law is trivial.
Theorem 10(b) is the dual of theorem 10(a) and is thus implied.
Theorem 10 implies that, if a smaller term appears in a larger term, then the larger term is redundant.
[10]
[9]

## Slide 24: Boolean Algebra
To illustrate the underlying concept of theorem 10 consider an example.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Example 5
By the absorption theorem, we have the expression simplified as
and
Theorem 11
The Proof of theorem 11(a) is done using the method of perfect induction. Theorem 11(b) is the dual of theorem 11(a) and is thus implied.
[11]

## Slide 25: Boolean Algebra
Theorem 12 (Consensus Theorem)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
The Proof of theorem 12(a) is done using the method of perfect induction. Theorem 12(b) is the dual of theorem 12(a) and thus proof is implied.
By theorem 12, if in a given Boolean expression we can identify two terms with one having a variable and the other having its complement, then the term that is formed by the product of the remaining variables in the two terms, in the case of a sum-of-products expression or by the sum of the remaining variables in the case of a product-of-sums expression will be redundant.
[12]

## Slide 26: Boolean Algebra
Example 6 Illustration of theorem 12.
Prove that
can be simplified to .
Solution.
appears in , appears in and appears in .
As a result, all three five-variable terms are redundant.
Also, variables C and D appear in all possible combinations, thus redundant.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 27: Boolean Algebra
Theorem 13 (DeMorgan’s Theorem)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
The Proof of DeMorgan’s theorem. Firstly, let us assume that all variables are in a logic ‘0’ state. In that case
Therefore, LHS = RHS.
Secondly, let us assume that any one of the n variables, say , is a logic HIGH state:
[13]

## Slide 28: Boolean Algebra
Once again LHS = RHS.
Therefore, theorem 13(a) stands proved. Since theorem 13(b) is the dual of theorem 13(a), the proof is implied.
DeMorgan’s theorems can thus be interpreted as follows: the first theorem says that a multi-input NOR gate can be implemented as a multi-input bubbled AND gate.
The second theorem, which is the dual of the first, says that a multi-input NAND gate can be implemented as a multi-input bubbled OR gate.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Theorem 14 (Involution Law)
Involution law says that the complement of the complement of an expression leaves the expression unchanged. Also the dual of the dual of an expression is the original expression.
[14]

## Slide 29: Boolean Algebra
Theorem 15 (Transposition Theorem)
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
This theorem can be applied to any sum-of-products or product-of-sums expression having two terms, provided that a given variable in one term has its complement in the other.
The proof of theorem 15(a) can be done using the method of perfect induction.
[15]
Figure 9: Example 7.

## Slide 30: Boolean Algebra
Example 7
Starting with the Boolean expression for a two-input OR gate, apply Boolean laws and theorems to modify it in such a way as to facilitate the implementation of a two-input OR gate by using two-input NAND gates only.
Solution.
A two-input OR gate has the Boolean equation ,
where A and B are the input logic variables and Y is the output.
Now, Involution law
DeMorgan’s theorem
Idempotent law
Figure 9 shows the NAND gate implementation of a two-input OR gate.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 31: Boolean Algebra
Example 8
Apply suitable Boolean laws and theorems to modify the expression for a two-input EX-OR gate in such a way as to implement a two-input EX-OR gate by using the minimum number of two-input NAND gates only.
Solution.
A two-input EX-OR gate has the Boolean equation ,
Now, Involution law
DeMorgan’s theorem
Figure 10 shows the NAND gate implementation of a two-input EX-OR gate.
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA

## Slide 32: Boolean Algebra
EX-OR gate
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA
Figure 10: Example 8.

## Slide 33: End of Lecture 2
Thank you for your attention!
Jerry MUWAMBA , DEPT. of EEE, School of Engineering, UNZA