## Slide 1: BASIC CONCEPTS AND PRINCIPLES OF MECHANICAL ROCK PENETRATION

## Slide 2
To appreciate the concepts and principles of drilling, one needs to understand:
Mechanics of rock penetration
Factors influencing penetration rate
Strength characteristics of rock
Rock type
  Homogeneous, Anisotropy, Isotropy

## Slide 3
Drillability factors
  Intrinsic environmental factors
    Geologic conditions
  State of stress of rock
  Internal structure of rock and resistance to penetration
6. Engineering properties

## Slide 4: Some terms related to rock disintegration include:
Force
Friction
Angle of friction
Torque
Resistance
Energy ; kinetic energy,
Compressive strength
Tensile strength
Stress
Shear stress
Strain
Stress/strain curve
Theories of elasticity
Thrust

## Slide 5
Force is a push or a pull on an object with mass that can cause it to change its velocity (to accelerate). A force is a vector, which means it has both magnitude and direction
Friction is the resistance to motion of one object moving relative to another. It is not a fundamental force. Friction is the force resisting the relative motion of solid surfaces, fluid layers, and material elements sliding against each other.
When a system expels or accelerates mass in one direction, the accelerated mass will cause a force of equal magnitude but opposite direction on that system. The force applied on a surface in a direction perpendicular or normal to the surface is called Thrust.
Torque is a twisting (torsion) or turning force that tends to cause rotation around an axis.
Energy is the capacity for doing work. It may exist in potential, kinetic, thermal, electrical, chemical, nuclear, or other various forms.
Stress is the force per unit area applied to the material. Tensile stress
Compressive stress
Young's modulus or modulus of elasticity is a measure of the ability of a material to withstand changes in length when under tension or compression. Young's modulus is equal to the longitudinal stress divided by the strain.

## Slide 6: Principles of Rock Disintegration
Rock drilling
For rock failure, energy is required
Enough energy to overcome rock strength
  Compressive strength (resistance)
Basically the energy (ɛ1) is required to penetrate or disintegrate the rock. The energy to overcome resistance should equal to the compressive strength per unit area
Force is applied on the rock by the bit
Bit-rock interface - under stress

## Slide 7: Fundamentals of mechanical rock penetration
Prime mover (drill) converts original form of energy into mechanical energy and the rod transmits the mechanical energy to the bit then to the rock:
Rotational effect creates torque
Percussive effect creates thrust
Torque and thrust create compressive stress
Bit and rock under compressive stress
The energy to overcome resistance should equal to the compressive strength per unit area
Compressive strength depends on Young’s modulus of a particular rock

## Slide 8: Fundamentals of rotary-percussive drilling
Percussion
Rotation
Feed or thrust load
Flushing

## Slide 9: Bit-rock interface
Bit
Rock
Drill rod

## Slide 10: Bit-rock interface

## Slide 11
Principles of Rock Disintegration

## Slide 12: Functional Components of Drilling System

## Slide 13: The Flushing Fluid
The circulation fluid is the flushing medium which is supplied through the flushing-holes in the drill steel and distributed through flushing-holes in the bit front.
The front of the bit has space for flushing the cuttings or chips rearwards.
The flushing medium may be air, water or mud.

## Slide 14: Principle of Drilling Fluid

## Slide 15: The Circulation Fluid
Cleans the hole
Cools the bit and
Stabilises the hole
Supports the penetration through removal of cuttings
Air, water or sometimes mud is used for this purpose.

## Slide 16: Drillability
Drillability means rate of drill bit penetration into rock [Tamrock..1983]. Schmidt R. L. [1972] defines drillability as the resistance of rock to penetration. Paithanker et al [1980] have shown that any stage of bit wear has a complex function of several rock properties, viz compressive strength, modulus of elasticity, density and coefficient of friction between rock and bit.

## Slide 17: Factors Affecting Drillability
Factors affecting the rate of penetration (drillability) include:
Rock properties
Drilling parameters
  Thrust
  Torque
  Flushing

## Slide 18: Rock properties influence on drillability
Among the important rock material properties having an over-all effect on the drilling techniques and drillability include:
Hardness
Abrasiveness
Texture
Structure

## Slide 19
Degree of rock hardness related to compressive strength of rock |  | 
Hardness | Mohs Level | MPa
Extremely hard | 7 and above | 200 and above
Hard | 6 - 7 | 120 - 200
Medium hard | 4 - 6 | 60 - 120
Somewhat soft | 3 - 5 | 30 - 60
Soft | 2 - 3 | 10 - 30
Extremely soft | 1 - 2 | 10 and below

## Slide 20: Consumption of drilling components
Drilling components including bits, rods, coupling sleeves, shank adapters wear out and become obsolete. The life-span of drilling components depends on:
Rock hardness
Abrasiveness
Texture
Structure
Hole diameter and length

## Slide 21: Drilling components

## Slide 22: Drilling components

## Slide 23
Revision Questions

## Slide 24
Q1. List five intrinsic environmental factors which affect the rate of rock penetration
Q2. In rock drilling, force of 15kN is applied on two circular bits with diameters 0.15m and 0.3m, calculate:
The stresses produced by each bit on the rock
Make comments on stresses produced
Which bit has high penetration rate
Q3. With reference to stress/strain curve, explain the behavior of rock under drilling forces and why the rock behavour is different from steel under the same forces.

## Slide 25
In rock drilling, force of 15kN is applied on two circular bits with diameters 0.15m and 0.3m, calculate:
The stresses produced by each bit on the rock
Make comments on stresses produced
Which bit has high penetration rate
Area bit 1 =
Load (force) =
Stress = Force/Area = 848. 8kNm2 for bit 1
Stress = 212.2kNm2 (for bit 2)
Bit I is producing more stress than bit 2 (3marks)
Bit is producing 4 times more stress than bit 2(5marks)

## Slide 26: Example: Consumption of drilling components
Calculate the required bits, rods, coupling sleeves, shank adapters and production in cubic metres given:
Tunnel length = 300m
Tunnel area = 40m2
Depth of round = 4.6m (with 95% advance)
Number of holes = 55 holes per round
Average service life:
45mm button bit = 300m
Coupling sleeves= 1,600m
Rods = 1,600m
Shank adapters = 2,500m

## Slide 27: Solution
Total drilled metres = Tunnel length x holes per round + 5% overdrill = (300 x 55) + (300 x 55 x 0.5) = 16,500 + 825 = 17,325m
Required bits = Total drilled metres/Average service life = 17,325/300 = 57.75 therefore 58 bits required
Required sleeves = 17,325/1,600 = 10.83; therefore 11 sleeves required
Required rods = 17,325/1,600 = 10.83; therefore 11 rods required
Required adapters = 17,325/2,500 = 6.93; therefore 7 adapters
Production = Area x Length = 40 x 300 = 12,000m3

## Slide 28
Assignment

## Slide 29
    Q1: Calculate the required:
      Bits;
      Shank adapters
      Sleeves; and
      Rods
    Given:
    Production = 1,000,000 tonnes
    Density = 4 tonnes/m3
    Specific drilling = 0.5
    Average service life (life span) of:
    51mm button bit = 450m
    Shank adapters = 3,500m
    Sleeves = 250m
    R32 rods = 150 holes
    R32 rod length = 1.8m

## Slide 30
Assignment
Hand in on Friday 16th July, 2021 before 12.00 hours
Email the assignment to: sam.kangwa@unza.zm
Show all the steps and calculations
Indicate the correct units
Type the assignment