## Slide 1
INTRODUCTION TO MINING ENGINEERING
By:
Dr. Sam Kangwa
Email: sam.kangwa@unza.zm

## Slide 2: RECAP
Mining terminologies
2. Five stages of the life of a mine
  Prospecting
  Exploration
  Development
  Exploitation
  Mine closure / reclamation
3. Mineral resources and mineral reserves

## Slide 3: RECAP
4. Classification of mining methods
5. Selection of mining methods
6. Surface mining
  Open pit mining
  Open cast mining
  Quarrying
  Auger mining
8. Underground mining and accessing underground
mineral deposits

## Slide 4: RECAP
7. Underground mining
  Self-supported
    Room and Pillar
    Sublevel open stoping
  Artificially supported
    Cut and fill
    VCR
  Caving methods
    Block caving
    Sublevel caving

## Slide 5
Tutorial or Revision Questions

## Slide 6
In surface and underground mining, the primarily purpose is to extract mineral
Ore deposit has to be fragmented
In order to break the rock, there is need to drill blast holes place in explosives and blast

## Slide 7: INTRODUCTION TO HARD ROCK DRILLING MECHANICAL ROCK PENETRATION

## Slide 8
BASIC PRINCIPLES OF DRILLING

## Slide 9: Unit Operations of mining
There are two types of unit operations of mining:
Production operations
Auxiliary operations

## Slide 10: Mining Unit Operation
The unit operations of mining are the basic steps used to produce mineral from the deposit, and the auxiliary operations that are used to support them. The steps contributing directly to mineral extraction are production operations, which constitute the production cycle of operations.

## Slide 11: Unit Operations
Auxiliary operations include:
Support
Ventilation
Power supply
Pumping
Maintenance
Communication

## Slide 12: Unit Operations
Units operations employed to produce minerals from deposits are:
Drilling
Blasting
Loading
Hauling
Production cycle = drill + blast + load + haul

## Slide 13
Drilling
Drilling is the first unit operation employed to produce ore, therefore need to understand basic principles of drilling.

## Slide 14: What is rock drilling?

## Slide 15: Definition of rock drilling
Rock drilling:
Mechanical rock penetration
Process of cutting or boring rock
Energy must be applied to the rock by direct or indirect means to fragment the rock
Energy is generated by rock drills

## Slide 16: Rock Drills
A rock drill is a drilling device designed specifically for penetrating rock.
A drill is a tool fitted with a cutting tool, usually a drill bit.
There are many types of rock drills including:
Electrical machines (electric drills)
Pneumatic drills (Compressed air machines)
Hydraulic drills

## Slide 17
Rock drills can be hand-held or attached to drill rigs.
Hand-held drills are manually controlled by an operator

## Slide 18: Hand- held rock Drills

## Slide 19: DTH Hydraulic Crawler Drill and Held-held Drill

## Slide 20: Boomer H120 Hydraulic Drilling Rig

## Slide 21: Rotary drill rig

## Slide 22: Core Drilling

## Slide 23: Purpose of Drilling
The general purpose of holes drilled include:
Prospecting
Exploration
  Core drilling
Anchorage, and
Blast holes

## Slide 24: Purpose of Drilling
For mining geologists, drill holes are specifically intended for:
Geological information
Establishment of stratigraphic column
Determination of presence of ore
Evaluation of ore and country rock
Estimation of tonnage and grade

## Slide 25: Purpose of Drilling
For mining engineers, drill holes are intended for:
Anchorage or support systems
Drainage, and
Blast holes
  The main purpose

## Slide 26: Blast-holes
The principle and economics of rock blasting in mining depends on the type and characteristics of drill-holes.
Explosives are loaded in the drill-holes and blasting techniques depends on:
Size of the blast-holes,
Depth, and
Spacing of drill-holes.

## Slide 27: Blast-holes
The choice of explosives and the size of the most economics drill-hole size and drilling depth is dictated by the cost of drilling.
The cost of drilling depends on penetration and wear characteristics of the rock.

## Slide 28: Drill Holes Characteristics
Drill holes are characterised by four factors:
Diameter
Length
Straightness
Stability

## Slide 29
Classification of drilling according to energy used:
Drilling is mainly done by mechanical attack, other methods of cutting holes according to energy used include:
Thermal hydraulic
Electric and Electromagnetic
Sonic high frequency vibration
Light-laser system

## Slide 30: Classification of Drilling
Classification according to principles of drilling:
Percussive action (hammer drills)
Rotary
Rotary-percussive

## Slide 31: Trends in Drilling
Advanced Drilling Methods
Better technology
  Machine design
  Machine efficiency
  Less lose of energy
Modern equipment
  Automated
  Safe
  Environmental control

## Slide 32: Trends in Drilling
Advanced Drilling Methods
Higher productivity
  Effective
  Low manpower
  High pay load
  High yield
Knowledge of mechanics of rock
  More knowledge of rock properties
  Properties affecting drilling

## Slide 33: Trends in Drilling Equipment
Basic drilling tools
  Application of hammer and chisel
Hydraulic drilling equipment
ITH high pressure drilling equipment
Diesel powered drilling equipment
Electro-hydraulic drilling equipment

## Slide 34: Automation of Drilling Equipment
Automated or computerized drilling
Eliminates the human factor
  Error in positioning and aligning
Rig orientates itself on its axis
Accurately collar and drill
Controls drilling parameters
Programmed coordinates, angles and depth
Optimum drilling of pattern of holes

## Slide 35: Automated Drilling rig

## Slide 36: Drilling Rig

## Slide 37: Factors Considered in Selection of Drilling Equipment
Length of holes
Diameter of holes
Rock characteristics
Drilling space
Source of drilling energy
Penetration rate
Safety

## Slide 38: Factors Affecting Drilling Performance
1. Operating variables (controllable factors)
  Drill power
  Speed
  Thrust
  Bit and rod design
  Blow energy and frequency

## Slide 39: Factors Affecting Drilling Performance
2. Rock factors (independent variables)
  Properties of rock
  Geologic conditions
  State of stress acting on the drill-hole
3. Service factors (external variables)
  Labour and supervision
  Power supply
  Job site

## Slide 40: Performance Parameters
In selecting the optimal drilling system or evaluating drill performance, four parameters are measured or estimated:
Process energy
Penetration rate
Bit wear
Cost
  Ownership + Operating = Overall Cost

## Slide 41: Revision Questions
Drilling technology has evolved from hand held pneumatic machines to automated drilling equipment. Explain how advanced drilling methods have affected the hole characteristics
List five units operations involved in stage four of the life of a mine
Describe four parameters considered in selection of optimal drilling system

## Slide 42: Revision Questions
Explain how bit wear affects drilling performance
Describe physical and mechanical properties which affect drilling performance
Describe how rock strength properties relate to energy required for mechanical rock penetration?
With reference to drilling performance, differentiate between rock factors and service factors