## Slide 1: GEE 4812: Principles of Geomatics
LECTURER : Mr. TWATAIZYA MINANGO
EMAIL : twataizya.minango@unza.zm
OFFICE : B.Eng. Main Building, 1st Floor, Former Zagis Offices, Room 2
Traverse Computations

## Slide 2: Content
Introduction
Booking Form
Loop Traverse Computation and Adjustment
Linear and Angular Misclosure
Calculation of Coordinates

## Slide 3: Loop Traverse
If the traverse formed by the survey lines closes at a station i.e. if the survey lines form a polygon or starts and finishes at the same survey station of the known co-ordinates then the traverse is known as closed traverse.
A closed traverse is generally used for locating the boundaries or for surveying large areas.

## Slide 4: Loop Traverse Computations
Consider the following loop traverse
Bearing AB =

## Slide 5
LOOP TRAVERSE (Booking Form)
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 

## Slide 6
LOOP TRAVERSE (Interior Angles)
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | A
Booking interior angles

## Slide 7
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 |  |  |  |  |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
The sum of measured angles =
Theoretically sum of interior angles = In this case n = 5, therefore sum of interior angles should be =
LOOP TRAVERSE (Sum of Angles)

## Slide 8
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 |  |  |  |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 |  |  |  |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 |  |  |  |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 |  |  |  |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 |  |  |  |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Correction per angle = 50”/5 angles = 10”
Angular Misclosure =
LOOP TRAVERSE (Angular Misclosure)

## Slide 9
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 |  |  |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 |  |  |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 |  |  |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 |  |  |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 |  |  |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum of Corrected angles =
LOOP TRAVERSE (Adjusted Angles)

## Slide 10
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 |  |  |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 |  |  |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 |  |  |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 |  |  |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bearing of line AB = as the line lies on the X access (see figure)
LOOP TRAVERSE (Bearing Calculations)

## Slide 11
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bearing calculation of other traverse legs
LOOP TRAVERSE (Bearing Calculations)

## Slide 12
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 |  |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 |  |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 |  |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 |  |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 |  |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 |  |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Initial bearing of line AB = Final bearing of line AB =
LOOP TRAVERSE (Bearing Calculations)

## Slide 13
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 |  |  |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 |  |  |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 |  |  |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 |  |  |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 |  |  |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum of distances (Traverse Legs) = 1239.00
LOOP TRAVERSE (Distances)

## Slide 14
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 |  |  |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Computation of Partials: and
LOOP TRAVERSE (Partials)

## Slide 15
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum of partials should be zero but and
That is and . We adjust using Bowditch method.
LOOP TRAVERSE (Sum of Partials)

## Slide 16
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 |  |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bowditch Corrections:
LOOP TRAVERSE (Bowditch Adjustment)

## Slide 17
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 |  |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bowditch Corrections:
LOOP TRAVERSE (Bowditch Adjustment)

## Slide 18
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 |  |  |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bowditch Corrections:
LOOP TRAVERSE (Bowditch Adjustment)

## Slide 19
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 |  |  |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 |  |  |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 |  |  |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bowditch Corrections:
LOOP TRAVERSE (Bowditch Adjustment)

## Slide 20
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 |  |  |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 |  |  |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 |  |  |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 |  |  |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 |  |  |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Bowditch Corrections:
LOOP TRAVERSE (Bowditch Adjustment)

## Slide 21
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
Computing adjusted and values : Difference in coordinates + adjustments
Correction =
LOOP TRAVERSE (Adjusted Partials)

## Slide 22
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 |  |  | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 | 0.00 | 0.00 |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
Note sum of partials equals to zero i.e and
Correction =
LOOP TRAVERSE (Sum of Adjusted Partials)

## Slide 23
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 | 3000.07 | 3155.10 | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 |  |  | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 |  |  | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 |  |  | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 |  |  | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 | 0.00 | 0.00 |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
We compute the coordinates of B that is and
Correction =
LOOP TRAVERSE (Calculation of Coordinates)

## Slide 24
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 | 3000.07 | 3155.10 | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 | 2827.72 | 3256.54 | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 | 2578.83 | 3256.71 | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 | 2560.04 | 3067.78 | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 | 3000.00 | 3000.00 | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 | 0.00 | 0.00 |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
We compute coordinates of the other points that is and
Correction =
LOOP TRAVERSE (Calculation of Coordinates)

## Slide 25
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 | 3000.07 | 3155.10 | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 | 2827.72 | 3256.54 | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 | 2578.83 | 3256.71 | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 | 2560.04 | 3067.78 | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 | 3000.00 | 3000.00 | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 | 0.00 | 0.00 |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
Note that the initial and final coordinates of A are the same.
Correction =
LOOP TRAVERSE (Calculation of Coordinates)

## Slide 26
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length m | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | - | - | - | - | - | - | - | - | - | 3000.00 | 3000.00 | A
B | ABC | 120 25 50 | +10 | 120 26 00 | AB | 00 00 00 | 155.00 | 0.00 | 155.00 | 0.07 | 0.10 | 0.07 | 155.10 | 3000.07 | 3155.10 | B
C | BCD | 149 33 50 | +10 | 149 34 00 | BC | 300 26 00 | 200.00 | -172.44 | 101.31 | 0.09 | 0.13 | -172.35 | 101.44 | 2827.72 | 3256.54 | C
D | CDE | 95 41 50 | +10 | 95 42 00 | CD | 270 00 00 | 249.00 | -249.00 | 0.00 | 0.11 | 0.17 | -248.89 | 0.17 | 2578.83 | 3256.71 | D
E | DEA | 93 25 50 | +10 | 93 26 00 | DE | 185 42 00 | 190.00 | -18.87 | -189.06 | 0.08 | 0.13 | -18.79 | -188.93 | 2560.04 | 3067.78 | E
A | EAB | 81 11 50 | +10 | 81 12 00 | EA | 98 48 00 | 445.00 | 439.76 | -68.08 | 0.20 | 0.30 | 439.96 | -67.78 | 3000.00 | 3000.00 | A
Sum = 539 59 10 90*(2n-4) = - 540 00 00 |  |  | +50 | 540 00 00 | AB | 00 00 00 Sum = | 1239.00 | -0.55 | -0.83 | 0.55 | 0.83 | 0.00 (Sum) | 0.00 (Sum) |  |  | 
 |  |  |  |  |  |  |  | +0.55 | +0.83 |  |  |  |  |  |  | 
error = 00 00 -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
L
R
Correction =
LOOP TRAVERSE (Booking Complete)

## Slide 27: Link Traverse
A link traverse is the type of traverse where an open type traverse is linked at the ends of an existing traverse so as to form a closed loop or closed traverse.
The closing line is generally defined by the coordinates at the endpoints which have been determined by the previous survey.

## Slide 28: Link Traverse Computations
Bearing AB
Bearing CD
Measured Angles | 
Station | Angle
B | 
E1 | 
E2 | 
E3 | 
E4 | 
D | 
Measured Angles | 
Station | Angle
B | 
E1 | 
E2 | 
E3 | 
E4 | 
D | 
Given the data below determine the coordinates of E1, E2, E3 and E4.

## Slide 29
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 |  |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 |  |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 |  |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 |  |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Measured Angles)

## Slide 30
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 |  |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 |  |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 |  |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 |  |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Sum of Measured Angles)

## Slide 31
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 |  |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 |  |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 |  |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 |  |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Computed Final Bearing)
Computed Final Bearing CD = initial bearing AB + sum of measured angles – (n x )
Where n = number of measured angles and is positive if even, negative if odd. f the result is negative, add .

## Slide 32
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 |  |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 |  |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 |  |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 |  |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Computed Final Bearing)
Computed Final Bearing CD
Computed Final Bearing CD

## Slide 33
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 |  |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 |  |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 |  |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 |  |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 |  |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Angular Misclosure)
Angular Misclosure = Computed Final Bearing CD – Known Final Bearing
A

## Slide 34
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 |  |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Angular Adjustments)
Correction per angle = 23”/6 angles = 3.83”

## Slide 35
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - |  |  | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Angular Adjustments)
Corrected Angles = Observed + Correction
Note that the corrected angles have been rounded off to the nearest second.

## Slide 36
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 |  |  |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Bearing Calculations)
Bearing of line A-B (Given)

## Slide 37
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 |  |  |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 |  |  |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 |  |  |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 |  |  |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 |  |  |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Bearing Calculations)
Bearing of line B-E1

## Slide 38
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Bearing Calculations)
Bearing calculation of other traverse legs.

## Slide 39
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 |  |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 |  |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 |  |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 |  |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 |  |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 |  |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Bearing Calculations)
Note : Computed bearing of line CD =

## Slide 40
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 |  |  |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 |  |  |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 |  |  |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 |  |  |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 |  |  |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Distances)
Sum of distances (Traverse Legs) = 3945.87

## Slide 41
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 |  |  |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Partials)
Computation of Partials: and

## Slide 42
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  |  |  |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LINK TRAVERSE (Sum of Computed Partials)
Sum of computed partials : and

## Slide 43
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Initial Partials =
LINK TRAVERSE (Initial Partials)

## Slide 44
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Linear Misclosure)
Initial Partials =
Error =

## Slide 45
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 |  |  |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Bowditch Adjustment)
Bowditch Corrections:
Initial Partials =
Error =

## Slide 46
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 |  |  |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Bowditch Adjustment)
Bowditch Corrections:
Initial Partials =
Error =

## Slide 47
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 |  |  |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 |  |  |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 |  |  |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 |  |  |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Bowditch Adjustment)
Bowditch Corrections:
Initial Partials =
Error =

## Slide 48
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 |  |  |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 |  |  |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 |  |  |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 |  |  |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 |  |  |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
Bowditch Corrections:
LINK TRAVERSE (Bowditch Adjustment)
Initial Partials =
Error =

## Slide 49
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 | 588.43 | -279.07 |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 | 867.03 | 83.29 |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 | 407.90 | -325.98 |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 | 1064.62 | -305.24 |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 | 793.30 | -42.77 |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 |  |  |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
Computing adjusted and values : Difference in coordinates + adjustments
LINK TRAVERSE (Adjusted Partials)
Initial Partials =
Error =

## Slide 50
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 | 588.43 | -279.07 |  |  | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 | 867.03 | 83.29 |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 | 407.90 | -325.98 |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 | 1064.62 | -305.24 |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 | 793.30 | -42.77 |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 | 3721.28 | -869.77 |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
Note: sum of adjusted partials and
LINK TRAVERSE (Sum of Adjusted Partials)
Initial Partials =
Error =

## Slide 51
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 | 588.43 | -279.07 | 4442.71 | 9093.91 | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 | 867.03 | 83.29 |  |  | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 | 407.90 | -325.98 |  |  | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 | 1064.62 | -305.24 |  |  | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 | 793.30 | -42.77 |  |  | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 | 3721.28 | -869.77 |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Calculation of Coordinates)
We compute the coordinates of E1 that is and
Initial Partials =
Error =

## Slide 52
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 | 588.43 | -279.07 | 4442.71 | 9093.91 | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 | 867.03 | 83.29 | 5309.74 | 9177.20 | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 | 407.90 | -325.98 | 5717.64 | 8851.22 | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 | 1064.62 | -305.24 | 6782.26 | 8545.98 | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 | 793.30 | -42.77 | 7575.56 | 8503.21 | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 | 3721.28 | -869.77 |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Calculation of Coordinates)
We compute coordinates of the other points that is and
Initial Partials =
Error =

## Slide 53
Stn | Angle | Observed Horizontal Angle | Correction | Corrected Horizontal Angle | Line | Bearing | Horizontal Length (m) | Difference in Coordinates |  | Adjustments |  | Adjusted Values |  | Coordinates |  | Point
 |  | ° ' " | " | ° ' " |  | ° ' " |  | ∆Y | ∆X | ∆Y | ∆X | ∆Y | ∆X | Y | X | 
A | - | - | - | - | A-B | 151 27 38 | - | - | - | - | - | - | - | 3854.28 | 9372.98 | B
B | A-B-E1 | 143 54 47 | -3.83 | 143 54 44 | B-E1 | 115 22 21 | 651.16 | 588.35 | -279.02 | 0.08 | -0.05 | 588.43 | -279.07 | 4442.71 | 9093.91 | E1
E1 | B-E1-E2 | 149 08 11 | -3.83 | 149 08 07 | E1-E2 | 84 30 28 | 870.92 | 866.92 | 83.35 | 0.11 | -0.06 | 867.03 | 83.29 | 5309.74 | 9177.20 | E2
E2 | E1-E2-E3 | 224 07 32 | -3.83 | 224 07 28 | E2-E3 | 128 37 56 | 522.08 | 407.83 | -325.95 | 0.07 | -0.04 | 407.90 | -325.98 | 5717.64 | 8851.22 | E3
E3 | E2-E3-E4 | 157 21 53 | -3.83 | 157 21 49 | E3-E4 | 105 59 45 | 1107.36 | 1064.48 | -305.16 | 0.14 | -0.08 | 1064.62 | -305.24 | 6782.26 | 8545.98 | E4
E4 | E3-E4-C | 167 05 15 | -3.83 | 167 05 11 | E4-C | 93 04 56 | 794.35 | 793.20 | -42.71 | 0.10 | -0.06 | 793.30 | -42.77 | 7575.56 | 8503.21 | C
C | E4-C-D | 74 32 48 | -3.83 | 74 32 44 | C-D | 347 37 41 | 3945.87 | 3720.79 | -869.48 | 0.49 | -0.29 | 3721.28 | -869.77 |  |  | 
Sum = 916 10 26 |  |  | -23 |  |  |  |  | 3721.28 | -869.77 |  |  |  |  |  |  | 
error = 00 00 23 |  |  |  |  |  |  |  | -0.49 | +0.29 |  |  |  |  |  |  | 
LINK TRAVERSE (Booking Complete)
L
R
Initial Partials =
Error =

## Slide 54
END